## Slide 1: High-Speed Track-and-Hold Circuit Design
October 17th, 2012
Saeid Daneshgar, Prof. Mark Rodwell (UCSB)
Zach Griffith (Teledyne)

## Slide 2
Outline
250 nm InP HBT technology review
Applications and Motivation
Key design features and contributions
Review of circuit design and layout
Measurement results and comparison

## Slide 3
TSC 250nm InP HBT Process
Four metal interconnect stack
Peak bandwidth of fmax = 700 GHz & ft=400 GHz
MIM caps of 0.3 fF/μm2
Thin-film resistors 50 Ω/square
Plot courtesy Zach Griffith, UCSB 250nm InP HBT, 2007

## Slide 4
Wideband Sample & Hold Applications
Sub-sampling applications: automated test equipment (ATE), oscilloscope, jitter measurement …
Slide courtesy MJC Teledyne
Undersampling applications: undersampling receivers
Direct conversion receiver:
  Problems such as DC offset, noise, distortion, I/Q mismatch, etc
Undersampling receiver:
  T/H replaces downconversion mixer
  Elimintaes IF filter, IF gain stages, mixer and high frequency LO
  DC offset, IQ mismatch problem goes away
  Noise folding is a problem

## Slide 5
Motivation: Sample & Hold vs Track & Hold

## Slide 6
High Frequency Sampling Techniques
Diode bridge: [1]
Wide bandwidth
Linearity
Dynamic Range
Switched Emitter Follower (SEF): [2]
Good linearity
Better dynamic range
 Stability issues with EF
Base-collector diode:
Widest bandwidth
Good linearity
Highest dynamic range
No stability issues
Flat AC response
[1] J. C. Jensen and L. E. Larson, “A broadband 10-GHz track-and-hold in Si/SiGe HBT technology,” IEEE JSSC, Mar. 2001.
[2] S. Shahramian, A. C. Carusone and S. P. Voinigescu, “Design Methodology for a 40-GSamples/s Track and Hold Amplifier in 0.18-μm SiGe
BiCMOS Technology,” IEEE JSSC, Oct. 2006.

## Slide 7
Key Design Features
Track & hold switch: base-collector diode lower Ron, lower Coff than HBT e-b junction
minority carrier storage time approximately equal to base transit time
Common reports in the literature: switch voltage swings set very small and fast,
but high IP3 only for fsignal <<fNyquist
Real-world design requires: switch voltages set for high IP3 with Nyquist-frequency input
Linearization of input buffer for high IP3 cubic feedforward path cancels IM3 from differential pair

## Slide 8
Input Buffer & TH Switch

## Slide 9
Input Buffer & TH Switch

## Slide 10
Nonlinearity Derivation - I
[1] W. Sansen, “Distortion in Elementary Transistor Circuits,” IEEE TCAS-II: Analog and Digital Signal Processing,
vol. 46, no. 3, pp. 315-325, Mar 1999.
[1]

## Slide 11
Nonlinearity Derivation-II

## Slide 12
Nonlinearity Derivation - III

## Slide 13
Output Buffer & Output Driver

## Slide 14
Output Buffer & Output Driver
Output buffer should always be on in Sample & Hold circuit
Output stage needs to be designed linear enough not to affect total nonlinearity of the circuit

## Slide 15
Layout (Signal path)
I.B.
O.D.
TH Switch
O.B.
TH Switch

## Slide 16
S-parameters measurement

## Slide 17
Clock Distribution Circuit

## Slide 18
Clock Distribution Circuit
Itail=6 mA
Itail=12 mA

## Slide 19
Clock Distribution Circuit - layout
LPB
HPB
HPB
C-H Amp.

## Slide 20
Transient and Linearity Measurements
10 GHz RF input signal with a 50 GHz clock
IIP3 & OIP3 vs Fin for Fclk = 50GHz

## Slide 21
THD and Beat test Measurements
Measured HD2 and HD3
40.002 GHz input signal is being sampled by
40 GSamples/s sampling rate.
P1dB

## Slide 22
Comparison with the State of the Art Works

## Slide 23
Questions?

## Slide 24
T&H Chip layout

## Slide 25
S&H Chip layout

## Slide 26
Sample & Hold Transient waveforms
10 GHz RF input signal is being sampled by a 50 GHz clock
Differential
Single-ended

## Slide 27
Sample & Hold Beat frequency test
Fin=20.5 GHz, Fclk=20 GHz
Fin=20.5 GHz, Fclk=10 GHz
Simulation
Experiment

## Slide 28
Sample & Hold Linearity Measurements
Calculated ENOB using simulated noise figure of 20dB is more than 6bits.

## Slide 29
Base-Collector Diode modeling - I
  D1:
  D2:
  D3:
  .

## Slide 30
Base-Collector Diode modeling - II
I-V Characteristic
Forward biased
I-V Characteristic
Reverse biased
Linear Scale
Log Scale