## Slide 1
1
Integrated Circuits for Wavelength Division De-multiplexing in the Electrical Domain
1H.C. Park, 1M. Piels, 2E. Bloch, 1M. Lu, 1A. Sivanathan, 3Z. Griffith, 1L. Johansson, 1J. Bowers, 1L. Coldren, and 1M. Rodwell
1University of California at Santa Barbara
2Technion, Israel Institute of Technology
3Teledyne Scientific & Imaging Company
23rd September, 2013
hcpark@ece.ucsb.edu
Notes: 1

## Slide 2
Outline
Motivation
2
New Proposed WDM Receivers
Test Setups and Results
  Two channel (SSB rejection) tests
  Three channel (adjacent channel rejection) tests
Conclusion

## Slide 3
Motivation
Network Traffics / High Data Rate Demands
  More bandwidth
  Higher spectral efficiency
  Low power consumption
  System complexity and cost
  Long reach
  Toward 1Tb/s using a Single Receiver (System)
System Directions:
  Coherent (phase/amplitude) modulations (i.e. 16QAM)
  Dual polarizations
  Gridless channels
  Super-channels
  Photonic and electronic Integrations
  Low power / high efficiency
3
High Speed Systems
High Efficiency Systems

## Slide 4
Conventional WDM Receivers
Configuration: Photonic IC + Electrical IC
  WDM multi-channels
  De-multiplexing using AWG
  Integrated LO lasers
  90° optical hybrids
  Balanced photo-diodes (PDs)
  EIC: TIAs + filters + ADCs + DSPs
4
Photonic IC
Complex PIC
Large die: expensive
Many interfaces between PIC & EIC
Fixed WDM channel spacing

## Slide 5
Proposed WDM Receivers
Single-chip Multi-channel WDM Receivers: Toward 1Tb/s
  Simple PIC: one LO + one optical hybrid + one set of PDs
  Complex EIC
    TIAs + filters + ADCs + DSPs
    SSB mixers
    Electrical LOs
    Challenges: high speed PDs1) and high speed EIC2)
5
Complex EIC: OK!!
Small and simple PIC
One set of interface between PIC & EIC
Flexible WDM channel spacing
EIC
References:
1) >300GHz PDs – Ishibashi et. al.
2) 1THz TRs – Jain Vibhor et. al.

## Slide 6
6
Two-Stage Down-conversion: Optical, then Electrical
2) Electrical LO for selected channel with SSB mixers
 Selected channel down-converted to near DC
3) Other channels removed by filtering
 Then, ADC + DSP
 DATA recovery
1) Optical LO for optical down conversion for all WDM channels
 Optical WDM channels become subcarriers in the electrical domain

## Slide 7
7
Ref. Agilent N4391A Optical Modulation Analyzer Measure with confidence
http://cp.literature.agilent.com/litweb/pdf/5990-3509EN.pdf
System Demonstration using OMA+EIC (2-channels)
Real-time
oscilloscope
OMA* as PICs
Free space optics
90° optical hybrid
& Balanced PDs
2-channel electrical IC
OMA* blocks
*OMA – optical modulation analyzer
As PICs

## Slide 8
8
Two-channel Tests: Single-side-band Suppression
Activated channel
Suppressed channel
(+) channel
(-) channel
(+/- channels)
I & Q outputs

## Slide 9
9
Two-channel Tests: Single-side-band Suppression
About 25dB SSB suppression
Negligible channel interference
x2 more channels within the PDs and EIC bandwidth
EIC outputs (Electrical Spectrum Analyzer)

## Slide 10
10
Three-channel Tests: Adjacent Channel Rejections
20GHz Spacing
10GHz Spacing
5GHz Spacing (no guard band)
*Measured spectrums by an optical spectrum analyzer
Tested with different channel spacing !!
(+/- channels)
I & Q outputs

## Slide 11
11
Three-channel Tests: Adjacent Channel Rejections
Eye Qualities with Different Filter Combinations
*Filter1: before optical modulators to suppress the side lobes
*Filter2: after EIC outputs to filter out the other channels
BER 1.0E-9

## Slide 12
Future Tests: 6-channel WDM Receivers
12
Concept schematics (PIC + EIC)
EIC for 6-channel receivers is ready to test !

## Slide 13
Future Tests: 6-channel WDM Receivers
6-channel WDM receiver IC
  Teledyne 500 nm InP HBT: ~300GHz ft , fmax
  1st design spin: no attempt to design for low power
  Simulations (5Gb/s BPSK)
    30Gb/s for BPSK, 60Gb/s for QPSK, 120Gb/s for 16QAM are feasible!
    6-channel initial EIC only tests (done)
    6-channel system demonstrations will be done (soon)!
13
4.8 x 1.5 mm2
±12.5GHz
I-output
Q-output
±37.5GHz
I-output
Q-output
±62.5GHz
I-output
Q-output

## Slide 14
The first concept demonstration using two channel EIC receivers
Spectral efficiency is maximized using a minimum channel spacing
5Gb/s using two channel receivers
Using 8-channels / 25GHz spacing / 100GHz EIC / 100GHz PDs / PDM
0.8Tb/s for QPSK, 1.6Tb/s for 16QAM
5GHz spacing data recovery
Flexible channel (<10GHz) designs
Future Works
6-channel demonstration soon
PIC + EIC demonstration soon
Silicon based designs in near future
Low power consumption
Small IC size
14
Conclusion

## Slide 15
15
Thanks for your attention!
Questions?
hcpark@ece.ucsb.edu