## Slide 1: A Tunnel FET Design for High-Current, 120 mV Operation
P. Long, J. Z. Huang, M. Povolotskyi, J. Charles, T. Kubis, G. Klimeck, Purdue University
D. Verreck, Imec, KU Leuven
M. J.W. Rodwell, University of California, Santa Barbara
B. H. Calhoun, University of Virginia, Charlottesville

## Slide 2: What does VLSI need ?
Want: low supply voltage → Steeper than 60mV/dec below threshold → Large dI/dV above threshold
Low voltage low switching energy CVDD2/2 .
Low leakage current thermal: Ioff ∝ exp(-qVDD/kT) want low VDD yet low Ioff .
Large on-current small delay CVDD /I .
Large on-current
Low leakage current

## Slide 3: Tunnel FETs: truncating the thermal distribution
Source bandgap truncates thermal distribution steep S.S.
T-FET
MOSFET
Must cross bandgap: tunneling low ION
Fix (??): GaSb/InAs broken-gap heterojunction
J. Appenzeller et al., IEEE TED, Dec. 2005

✘

## Slide 4: Tunnel FETs: are prospects good ?
Useful devices must be small: short gate→ thin channel
Quantization shifts band edges→ tunnel barrier
Confinement also increases effective masses Transmission , where ~10% for a 2nm barrier, 1% for a 4nm barrier
What actual on-current might we expect ?

## Slide 5: T-FET on-currents are low, T-FET logic is slow
3.0%
NEMO simulation: GaSb/InAs tunnel finFET: 2nm thick body, 1nm thick dielectric @ er=12, 12nm Lg
10 mA/mm
Experimental: InGaAs heterojunction HFET; Dewey et al, 2011 IEDM, 2012 VLSI Symp.
~15 mA/mm @0.7V
Low current → slow logic
How to increase on-current?

## Slide 6: Increasing the on-current
P. Long et al., EDL 3/2016
S. Brocard, et al., EDL, 2/2014
Reduces tunnel barrier height
Reduces hole mass
Reduces tunnel barrier thickness
Adds resonant state
Reduces tunnel barrier thickness
Adds resonant state
Avci & Young, (Intel) 2013 IEDM
P. Long et al., EDL 3/2016

## Slide 7: [110] gives more on-current than [100]
high confinement mass low transport mass
low confinement mass high transport mass
Valence Band
P. Long et al., EDL 3/2016

## Slide 8: [110] gives more on-current than [100]
larger hole confinement mass→ smaller barrier→ more current smaller hole transport mass→ more current
larger tunnel barrier
smaller tunnel barrier
smaller m*
larger m*
thinner barrier
greater transmission
P. Long et al., EDL 3/2016

## Slide 9: Heterojunctions increase the junction field
Added heterojunctions→ greater built-in potential→greater field→ thinner barrier
Source heterojunction: S. Brocard, et al., EDL, 2/2014; Channel heterojunction: P. Long et al., EDL 3/2016

## Slide 10: Heterojunctions increase the tunneling probability
Added heterojunctions→ greater built-in potential→greater field→ thinner barrier
Source heterojunction: S. Brocard, et al., EDL, 2/2014; Channel heterojunction: P. Long et al., EDL 3/2016

## Slide 11: Heterojunctions increase the on-current
Added heterojunctions→ greater built-in potential→greater field→ thinner barrier
Source heterojunction: S. Brocard, et al., EDL, 2/2014; Channel heterojunction: P. Long et al., EDL 3/2016
Ballistic simulations

## Slide 12: Role of the resonant bound states: ON-state
On-state: bound states increase transmission
10-1
10-3
10-5
101
local density of states, 1/eV
Transmission > 50% over 80meV

## Slide 13: Role of the resonant bound states: OFF-state
Phonon scattering:
  Off-sate: evanescent tails of bound states  leakage between two states → Keep the bound state energies near the well edge energies

## Slide 14: Lg=30nm: Ioff limited by scattering
scattering
At 30nm Lg , VDD must be increased ~0.07V to maintain on/off ratio
At 15nm Lg , on/off ratio limited by S/D tunneling
S/D tunneling
Lg=15nm: Ioff limited by S/D tunneling
60mV/dec
60mV/dec
0.04
Simulations use 220meV/nm optical deformation constant , consistent with m=1.1x105 cm2V‑1s-1.
need Vgs running up to (?) 120mV

## Slide 15: Leakage at Lg=15nm
Local current density
(absolute value of current)
A/(m*eV)
Vg1 (close to off): current limited by S/D tunneling
Vg2: current limited by phonon scattering
S/D tunneling
Phonon scattering
Vg1
Vg2
Vg1
Vg2
0.04
Current(A/m)
1016
1014
1012
1010
need Vgs running up to (?) 120mV

## Slide 16: Phonon-Assisted Tunneling: 3HJ-TFET
S.S. and Ioff increased with intensity of phonon scattering
Vth shifted
Vth not shifted

## Slide 17: Phonon-Assisted Tunneling: TFET vs. 3HJ-TFET
Even with P.A.T., 3HJ design provides much larger ION than TFET
Vth shifted

## Slide 18: Noise margin sets a minimum threshold voltage
Need high voltage gain dVout/dVin at switching point
→ FET ID-VDS curve should be saturated (flat) at the switching point
Vin=VDD
Vin=3/4VDD
Vin=1/2VDD
Vin=1/4VDD
Vin=0
Vin=1/4VDD
Vin=1/2VDD
Vin=3/4VDD
Vout
ID
Gain = dVout/dVin =

## Slide 19: EF,drain should be below Ec at switching point
Need low output conductance when biased at switching point output conductance: from drain-source reverse injection to avoid : need drain Fermi level below channel conduction band must decrease (Vgs-Vth ) → increase Vth
Increasing the threshold voltage: Improves the noise margin Reduces ION. Also reduces IOFF
✘


## Slide 20: EF,drain should be below Ec at switching point
Need low output conductance when biased at switching point output conductance: from drain-source reverse injection to avoid : need drain Fermi level below channel conduction band must decrease (Vgs-Vth ) → increase Vth
Increasing the threshold voltage: Improves the noise margin Reduces ION. Also reduces IOFF
Fix graphs
Vth increased xx mV

## Slide 21: Increasing Vth increases noise margin
SP1: FET not saturated large dID/dVDSlow gain, small noise margin
SP2: Vth increased 20 mVFET is just saturated. Small dID/dVDS large gain, large noise margin
Increasing Vth deceases Ion from 106 A/m to 60A/m at VDD=0.08V
SP1
SP2
Fix graph

## Slide 22: Tunnel FET Design for High-Current, 120 mV Operation
Low-energy computing is low-voltage computing
MOSFETs: 60 mV/dec. set minimum ~500mV operation. Tunnel FETs: subthreshold swing < 60 mV/dec. small on-currents→ slow logic ~120mV operation→ extremely slow logic
Triple-heterojunction FETs: increased junction field, resonant states. >50% tunneling probability; full energy range N-TFET & PTFET designs. Designs using semiconductors with good high-K's.
Future work: modeling leakage: scattering, defects.
you have all the wrong words here

## Slide 23
(end)

## Slide 24: P-Channel designs
P-TFET performance is similar to that of the N-TFET
J. Huang et al., in review (also arXiv preprint 1605.07166)
6.1 Å design: No demonstrated high-quality dielectrics
InP-based design: channel is InAs/InGaAs/InP Some unpublished UCSB data suggesting good high-K interfaces on p-type InGaAs (Chobpattana, Stemmer) working to verify now Simulations: (10-3 A/m IOFF, 300 mV VDD) 6.1 Å design: 580 A/m Ion. comparable to N-TFET InP design: not yet simulated.
J.Z. Huang, et al, J-EDS, Vol 4, No.6, Nov 2016

## Slide 25: Designs compatible with high-quality dielectrics
Triple-heterojunction design can be realized with high-quality dielectrics.
Present designs can be further improved.
P. Long et al., 2016 IEEE IPRM conference
6.1 Å design: No demonstrated high-quality dielectrics
InP-based design: channel is InAs/InGaAs/InP high-quality dielectrics for all of these Chobpattana, Stemmer, APL, 2014. MOSFETs: 61 mV/dec. InAs, 65mV/dec. InGaAs 67mV/dec. InP
Simulations: (10-3 A/m IOFF, 300 mV VDD) InP design: 380 A/m Ion. 6.1 Å design: 800 A/m Ion. (need to improve design)

## Slide 26: Performance comparisons (ideal ballistic case)
70 mV operation→ 100:1 less switching energy than 700 mV CMOS 3HJ TFET @ 70 mV: 6.7:1 slower than CMOS GaSb TFET @70 mV: 1200:1 slower than CMOS
Design | VDD | relative switching energy ∝VDD2 | Ion@ 10-3 A/m Ioff | speed F.O.M. Ion/VDD
Si NMOS (experimental) | 700 mV | 1 | ~1000 A/m | ~1400 S/m
Si NMOS (simulated) | 700 mV | 1 | 4080 A/m | 5830 S/m
GaSb/InAs TFET | 300 mV | 0.18 | 32 A/m | 107 S/m
GaSb/InAs TFET | 70 mV | 0.01 | 0.34 A/m | 4.86 S/m
3HJ-TFET; 0.3V design | 300 mV | 0.18 | 800 A/m | 2670 S/m
3HJ-TFET; 70mV design | 70 mV | 0.01 | 61 A/m | 871 S/m
Caveats: Simulations ignore scattering: with it, what performance will we then obtain ? Structure is complex: can we make it ? Can we reduce threshold variations, or at least compensate for them ?
Lg=30nm