## Slide 1: Wireless Above 100GHz
Mark Rodwell, University of California, Santa Barbara Ali Niknejad University of California, Berkeley
Radio and Wireless Week, January 14, 2018, Anaheim, CA

## Slide 2: Why 100+ GHz wireless ?

## Slide 3
140-340 GHz properties

## Slide 4: 140-340 GHz: benefits & challenges
Massive # parallel channels
Need mesh networks
Need phased arrays (overcome high attenuation)
4
Large available spectrum
spatial multiplexing
(note high attenuation in foul weather)
line-of-sight MIMO

## Slide 5: Spatial Multiplexing: massive capacity RF networks
multiple independent beams each carrying different data each independently aimed # beams = # array elements small: 1000 elements @220 GHz=3 square inches
Hardware: multi-beam phased array ICs

## Slide 6: mm-Wave LOS MIMO: multi-channel for high capacity
Torklinson : 2006 Allerton Conference Sheldon : 2010 IEEE APS-URSI Torklinson : 2011 IEEE Trans Wireless Comm. 2012 IEEE Marconi prize paper award
Massive capacity wireless; physically small

## Slide 7: 140-340GHz imaging: TV-like resolution
What you see in fog
What 10GHz radar shows
What you want to see
goal: ~0.2o resolution, 103-106 pixels
NxN phased array
mm-waves → high resolution from small antenna apertures
angular resolution = l /D (radians) 340 GHz, 35 cm/14 inch aperture → 0.14 degree resolution
D
D
HDTV-like resolution, yet fits in car, plane, or UAV

## Slide 8
140-340 GHz applications

## Slide 9: 140-340GHz: high-capacity communications
Gigabit mobile communication.
Mobile information Access
Gigabit residential/office communication.
Cellular/internet convergence

## Slide 10: 140-340GHz: automotive applications
340 GHz HDTV-resolution sub-mm-wave imaging radar: see through fog and rain. assist driver: drive safely in fog at 100 km/hr self-driving: complements LIDAR, but works in bad weather.
60 GHz Doppler / ranging radar. object near ? approaching ? Avoid collision.
Intelligent highway: coordinate traffic anticipate & manage interactions, avoid collisions

## Slide 11: 140-340 GHz: sensing and imaging radar
Radar: See threats through fog/smoke/dust, when you can't see in the optical.
30/70/ 94 GHz early-warning radar: threat detection = something is there Longer range→ lower resolution: something's there, can't tell what.
140-340GHz imaging radar: threat identification= what is it ? Shorter range (500m in fog), TV-like resolution. Small and light.
Fog, dust, smoke: what you see
What 10GHz radar shows
What you want to see
Imaging for UAVs, drones, small planes. small, light aperture, high resolution. sub-mm-wave SAR: see through fog, optical-like resolution, kilometers range mm-wave PAR: imaging/ranging/Doppler

## Slide 12
140-340 GHz: Possible Systems

## Slide 13: 140/220 GHz spatially multiplexed base station
1 Tb/s spatially-multiplexed base station 256 users/face, 4 faces 1024 total users @ 1 user/beam, 1 Gb/s/beam; 200 m range
Link budget is feasible, but... Required component dynamic range ? Required complexity of back-end beamformer ?

## Slide 14: 140 GHz spatially multiplexed base station
Each face supports 256 beams @ 1Gb/s/beam.
100 meters range in 50 mm/hr rain
PAs: 16 dBm Pout (per element)
LNAs: 3 dB noise figure
Realistic packaging loss, operating & design margins

## Slide 15: 140/220 GHz femtocells

## Slide 16: 340 GHz or 650 GHz backhaul
Sub-mm-wave line-of-sight MIMO network backbone wireless @ optical speed; backhaul when you can't run fiber 340 GHz: 640Gb/s @ 240 meters; 1.2 meter, 8-element array 650 GHz: 1.28Tb/s @ 240 meter; 1.2 meter, 16-element array
linear array
square array

## Slide 17: 340 GHz 640 Gb/s MIMO backhaul
1.2m MIMO array: 8-elements, each 80 Gb/s QPSK; 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
250 meters range in 50 mm/hr rain; 29 dB/km
PAs: 10 dBm Pout (per element)
LNAs: 4 dB noise figure
Realistic packaging loss, operating & design margins

## Slide 18: 340 GHz frequency-scanned imaging car radar
Image refresh rate: 60 Hz
Resolution 64×512 pixels
Angular resolution: 0.14 degrees
Aperture: 35 cm by 35 cm
Angular field of view: 9 by 73 degrees
Component requirements: 35 mW peak power/element, 3% pulse duty factor 6 dB noise figure, 5 dB package losses 5 dB manufacturing/aging margin
Range: see a soccer ball at 300 meters (10 seconds warning) in heavy fog (15 dB SNR, 35 dB/km, 30cm diameter target, 10% reflectivity, 100 km/Hr)

## Slide 19
Transistors & ICs

## Slide 20: IC Technologies for 100 + GHz systems
Si VLSI CMOS, SiGe HBT Baseband signal processing at any carrier frequency high-frequency interfaces to ~220 GHz low power, high noise → long range needs large arrays.
GaN High-power amplifiers for long-range links Several Watts @94 GHz, likely will evolved to Watts at 220 GHz
InP HBT up/downconvert to 340, 650 GHz from 220 GHz Si VLSI medium-power amplifiers at 140, 220 GHz.
InP MOS-HEMT Lowest-noise amplifiers at any frequency low receiver noise→ less transmit power→ less system power

## Slide 21: mm-Wave Wireless Transceiver Architecture
custom PAs, LNAs → power, efficiency, noise Si CMOS beamformer→ integration scale
...similar to today's cell phones.

## Slide 22: mm-wave CMOS (examples)
260 GHz amplifier, Feedback-enhanced-gain: 65nm bulk CMOS, 2.3 dB gain per stage (350GHz fmax) Momeni ISSCC, March 2013
145 GHz amplifier, conventional neutralized design: 45 nm SOI CMOS, 6.3 dB gain per stage Kim et al. (UCSB), unpublished
350 GHz fmax

## Slide 23: mm-Wave CMOS won't scale much further
Gate dielectric can't be thinned → on-current, gm can't increase
Tungsten via resistances reduce the gain
Inac et al, CSICS 2011
Shorter gates give no less capacitance dominated by ends; ~1fF/mm total
Maximum gm, minimum C→ upper limit on ft. about 350-400 GHz.
Present finFETs have yet larger end capacitances

## Slide 24: III-V high-power transmitters, low-noise receivers
Cell phones & WiFi: GaAs PAs, LNAs
mm-wave links need high transmit power, low receiver noise
0.47 W @86GHz
0.18 W @220GHz
1.9mW @585GHz
M Seo, TSC, IMS 2013
T Reed, UCSB, CSICS 2013
H Park, UCSB, IMS 2014

## Slide 25: 130nm / 1.1THz InP HBT Technology
Teledyne: M. Urteaga et al: 2011 DRC
Rode (UCSB), IEEE TED, 2015
3.5 V breakdown

## Slide 26: 130nm / 1.1THz InP HBT: IC Examples
Teledyne: M. Urteaga et al: 2017 IEEE Proceedings
Integrated ~600GHz transmitter
220 GHz 0.18W power amplifier
UCSB/Teledyne: T. Reed et al: 2013 CSICS
325 GHz power amplifier
UCSB/Teledyne: (being tested)

## Slide 27: InP HBT: Towards the 2 THz / 64nm Node
Narrow junctions. Thin semiconductor layers High current density Ultra low resistivity contacts
Yihao Fang, UCSB, unpublished

## Slide 28
HEMTs: key for low noise
Hand-derived modified Fukui Expression, fits CAD simulation extremely well.
2:1 to 4:1 increase in ft → improved noise
→ less required transmit power→ easier PAs, less DC power
or enable higher-frequency systems

## Slide 29
HEMTs: State of the art
Xiaobing Mei, et al, IEEE EDL, April 2015 (Northrop-Grumman)
First Demonstration of Amplification at 1 THz Using 25-nm InP High Electron Mobility Transistor Process

## Slide 30
Towards faster HEMTs
Gate barrier: Key scaling limit Solution replace InAlAs barrier with high-K dielectric Target ~10nm node ~0.5nm EOT, ~1.5 THz ft.
Jun Wu, UCSB, unpublished

## Slide 31
Systems & Packages

## Slide 32: Beamforming for massive spatial multiplexing
Pure digital beamforming: massive dynamic range throughout signal chain massive computational complexity
Pure RF beamforming: (focal plane, Butler matrixes, RF beamforming) Physically complex. Component precision. Lack of adaptation.
Likely best approach is tiled Butler or RF beamforming in the tile. Analog or digital in overall array

## Slide 33: Sectoral phased arrays for size, dynamic range
At a given beamwidth and a given angular steering range, as we increase the # of sectors, we increase the element size (and array size), and reduce the # of beams per sector.
mm-wave arrays become easier to construct Dynamic range is vastly improved.

## Slide 34: The mm-wave module design problem
How to make the IC electronics fit ? 100+ GHz arrays: l0/2 element spacing is very small. Antennas on or above IC → IC channel spacing = antenna spacing → limited IC area to place circuits
How to avoid catastrophic signal distribution losses ? long-range, high-gain arrays: array size can be large. ICs beside array → very long wires between beam former and antenna → potential for very high signal distribution losses
How to remove the heat ? 100+ GHz arrays: element spacing is very small. If antenna spacing = IC channel spacing, then power density is very large

## Slide 35: background: split-block waveguides
Waveguides are manufactured (milled or die cast) from a set of pieces
Precision pins aid alignment

## Slide 36: Concept: Tile for mm-wave arrays
Split-block assembly. Modules tile into larger array
IC area can be much larger than antenna area→ electronics can fit
Low-loss waveguide feeds, efficient waveguide horn antennas
Efficient heat-sinking: permits W-level GaN, InP, SiGe PAs for long range

## Slide 37
Wireless Above 100 GHz

## Slide 38: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-silicon for short ranges below 250 GHz. III-V LNAs and PAs for longer-range links. Just like cell phones today III-V frequency extenders for 340GHz and beyond
The challenges spatial multiplexing: computational complexity, dynamic range packaging: fitting signal channels in very small areas

## Slide 39
(backup slides follow)

## Slide 40
Talk is 30 min plus 10 min for questions… 25-30 slides