## Slide 1: IC, Package, and System Technologies for 140GHz MIMO hubs and 210/280GHz MIMO backhaul links
Mark Rodwell, Ahmed Ahmed, Ali Farid, Utku Solyu, University of California, Santa Barbara Munkyo Seo Sungkyunkwan University (on sabbatical at UCSB)
This work was supported in part by the Semiconductor Research Corporation (SRC) and DARPA.
Silicon Monolithic Integrated Circuits in RF Systems (SiRF2021), San Diego, CA, 21 January 2021

## Slide 2: Beyond-5G Wireless
ComSenTer: 100-300GHz carriers, massive spatial multiplexing → Terabit hubs and backhaul links, high-resolution imaging radar
Wireless networks: exploding demand.
Immediate industry response: 5G. ~10-100GHz carriers. increased spectrum, extensive beamforming
Next generation (6G ??): above 100GHz.. greatly increased spectrum, massive spatial multiplexing
JUMP Centers: research commercialized in 15 years

## Slide 3: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 4
100-300 GHz: Applications

## Slide 5: 100-300GHz: Demonstration Systems
MIMO hub: 140GHz
Point-point MIMO: 210, 280GHz
Cross-linear-array imaging: 210, 280GHz
UCSB FCC permit: 137 +/- 15 GHz, 210 +/- 15 GHz, 280 +/- 15 GHz

## Slide 6: 140GHz massive MIMO hub
0.5-5 Tb/s spatially-multiplexed 140GHz base station 128 users/face, 4 faces. P1dB=21 dBm PAs, F=8dB LNAs 512 total users @ 1 user/beam, 1,10 Gb/s/beam; 230, 100 m range in 50mm/hr rain with 17dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 7: 140GHz moderate-MIMO hub
If demo uses 32-element array (four 1×8 modules): 16 users/array. P1dB=21 dBm PAs, F=8dB LNAs 1,10 Gb/s/beam→ 16, 160 Gb/s total capacity 40, 70 m range in 50mm/hr rain with 17dB total margins
Range varies as (# hub elements)0.5 → (Service area/element) is constant
Handset: 8 × 8 array (9×9mm)

## Slide 8: 210 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 3.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 18dBm =P1dB (per element) LNAs: 6dB noise figure

## Slide 9
Overall ComSenTer Research

## Slide 10: ComSenTer: Wireless Research
Elad Alon
UC Berkeley
Upamanyu
Madhow
UC Santa Barbara
James Buckwalter
UC Santa Barbara
Systems
Borivoje Nikolic
UC Berkeley
Vladimir
Stojanovic
UC Berkeley
Ali Niknejad
UC Berkeley
Mark Rodwell
UC Santa Barbara
Umesh Mishra
UC Santa Barbara
Srabanti Chowdhury
UC Davis
Gabriel Rebeiz
UC San Diego
Sundeep
Rangan
Susanne Stemmer
UC Santa Barbara
ICs
Transistors
N-polar GaN HEMTs for 140, 210GHz
AlN/GaN HEMTs for 140, 210GHz
GaN HEMTs on Si
Diamond cooling for GaN
Networks, Applications, MIMO, Power
MIMO algorithms Imaging algorithms Compressive imaging
MIMO algorithms VLSI MIMO processors
mm-wave CMOS: hub mm-wave arrays mm-wave MIMO
mm-wave CMOS: handset mm-wave arrays
efficient PAs III-V arrays
Kenneth O
UT Dallas
Dina Katabi
MIT
Harish Krishnaswamy
Columbia
Alyosha Molnar
Cornell
Debdeep Jena
Cornell
Huili (Grace) Xing
Cornell
Christoph Studer
Cornell
Amin Arbabian
Stanford
Andreas Molisch
USC
Hossein Hashemi
USC
N-path mixers MIMO ADCs
200-300GHz passive CMOS
design automation equalizers
photonic links
transistors in novel materials
THz HBTs for PAs THz HEMTs for LNAs
100-300GHz propagation measurements
Applications: VR, cars, …
STAR Novel MIMO
acoustic filters
VLSI design automation VLSI MIMO processors
140GHz radar chipsets and arrays
Massive MIMO demo.
Compressive imaging
140/210/290GHz arrays for demos.
Danijela Cabric
UCLA
MIMO algorithms

## Slide 11: ComSenTer Research: Systems
ADCs/DACs: only 3-4 bit ADC/DACs required (Madhow, Studer)
Linearity: Amplifier P1dB need be only 3dB above average power (Madhow).
Phase noise: Requirements same as for SISO (Alon, Madhow, Niknejad, Rodwell)
Efficient digital beamforming: beamspace algorithm=complexity ~N× log(N) (Madhow, Studer)
Efficient digital beamforming: low-resolution matrix (Studer, Molnar)
Efficient channel estimation : fast beamspace algorithm (Studer)
Efficiently addressing true-time-delay problem: "rainbow" FFT algorithm (Madhow, Cabric)
Digital beamforming:
Other issues:
Propagation models and measurements
Blockage probability, mesh networks, network protocols

## Slide 12: ComSenTer Research: ICs
140GHz 8-element handset TRX, RCVR arrays and PAs Rebeiz
280GHz CMOS upconvert mixers 420 GHz CMOS receiver O
210GHz InP transceivers and arrays, 210, 280GHz PAs Seo/Rodwell
Hydra digital processor (beamformer) Nikolic
Beamspace digital beamformer Studer/Molnar
60GHz CMOS channel aggregation transceiver Krishnaswamy
Record-PAE Class B 140GHz PAs Buckwalter
Record-PAE Class A 100-200mW 140GHz PAs Rodwell
140GHz CMOS handset ICs Rodwell
Not shown: 140GHz, 210GHz outphasing transmitters Buckwalter mm-wave N-path mixers Molnar GaN active circulators Krishnaswamy 140GHz GaN PAs Buckwalter
75GHz MIMO front-ends Niknejad, Alon, Nikolic

## Slide 13: ComSenTer Research: Demos
Hydra digital processor Nikolic
140GHz MIMO hub modules UCSB
ICs for 210GHz Demo Rodwell
BWRC Testbed: RF: 75GHz BWRC & 140GHz UCSB Digital: FPGA, COTS Hydra, ASIC Hydra
NYU Testbed: RF: 60GHz SDR (NYU) & 140GHz UCSB Digital: FPGA
75GHz MIMO Module Niknejad
75GHz MIMO IC Niknejad
120GHz MIMO link Niknejad
130GHz MIMO link Arbabian

## Slide 14
140GHz ICs and Modules

## Slide 15: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 16: 140GHz hub: packaging challenges
IC-package interconnects Difficult at > 100 GHz
Removing heat Thermal vias are marginal
Interconnect density Dense wiring for DC, LO, IF, control. Hard to fit these all in.
Economies of scale Advanced packaging standards require sophisticated tools High-volume orders only Hard for small-volume orders (research, universities) Packaging industry is moving offshore

## Slide 17: 100-300GHz IC-package connections
type | Frequency | technology | cost | heatsinking
micromachined waveguide interface | 1000 GHz | Research. Cheap one day ? | high ✘ | good
ribbon, mesh bond | 200 GHz | Handcrafted. | high ✘ | good
patch antennas on superstrate | 1000 GHz | Straightforward | low | good
Cu stud flip-chip | >200 GHz | Industry standard | low | ok, marginal for PA ✘
hot vias | 200 GHz | Development | low ? | good
(ball) wirebonds | 100 GHz ✘ | Industry standard | low | good
Deal, IEEE Trans THz, Sept 2011
G. Rebeiz

## Slide 18: Cu Pillars vs. C4 Solder-bonds
Cu pillars: Small geometry: 50 mm diameter Excellent 140GHz characteristics: ~0.7dB loss without tuning. Requires solder mask with very small openings (<75 mm). Requires tight lithographic resolution on interposer.
C4 bonds: Readily handled by LTCC and PCB board and assembly firms. 140GHz parasitics require impedance-tuning on LTCC carriers. 0.5dB loss feasible after tuning

## Slide 19: 140GHz massive MIMO hub modules
LTCC-based array tile
Kyocera LTCC carrier
connector interface board
140GHz CMOS ICs
transmit
receive
140GHz InP PAs
8 CMOS ICs, 8 InP PAs
connector interface board
Farid, Ahmed, Rodwell, UCSB; Flynn, Dunn, Niknejad, Nikolic, BWRC; Rebeiz, UCSD
Psat ~100mW
…
…

## Slide 20: 140GHz hub: ICs & Antennas
110mW InP Power Amplifier 20.8% PAE
190mW InP Power Amplifier 16.7% PAE
CMOS Transmitter IC 22nm SOI CMOS.
Receiver IC 22nm SOI CMOS.
LTCC Array module
1 cm
Teledyne InP HBT
GlobalFoundries 22nm SOI CMOS
Kyocera

## Slide 21: 140GHz Receiver, GlobalFoundries 22nm SOI CMOS
1.9 mm
0.76 mm
A. Farid UCSB, 2019 RFIC symposium
~15GHz bandwidth, ~8dB Noise Figure

## Slide 22: 140GHz Transmitter, GlobalFoundries 22nm SOI CMOS
1.9 mm
0.76 mm
A. Farid UCSB, 2019 RFIC symposium
~10GHz bandwidth, ~2dBm output power

## Slide 23: 140GHz InP PA: 20.5dBm, 20.8% PAE
A. S. Ahmed UCSB, 2020 IMS
1.08 mm x 0.63 mm
Teledyne 250nm InP HBT
Capacitively-degenerated common-base stages
17dBm, 9.7% PAE @ P1dB

## Slide 24: 140GHz InP PA: 23dBm, 17.8% PAE
A. S. Ahmed UCSB, 2020 EuMiC
1.23 mm x 1.09 mm
Teledyne 250nm InP HBT
Capacitively-degenerated common-base stages
20.2dBm, 9.4% PAE @ P1dB

## Slide 25: 140GHz Single-Channel CMOS-Only Transmitter
A. Farid, A. S. Ahmed, UCSB, results in review

## Slide 26: 140GHz Single-Channel CMOS+InP Transmitter
A. Farid, A. S. Ahmed, UCSB, modules being tested

## Slide 27: 140GHz 8-Channel All-CMOS Transmitter Array
Presently learning how to assemble complex modules…

## Slide 28
210GHz ICs and Modules

## Slide 29: 210 GHz MIMO backhaul demo
8-element MIMO array 3.1 m baseline for 500m link. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 63mW =P1dB (per element) LNAs: 6dB noise figure

## Slide 30: InP ICs for 210GHz Point-Point MIMO
Transceivers & Arrays for 210GHz MIMO links
2/2020 tapeout: 210 GHz TX front-end w/ +20 dBm Psat 210 GHz TX front-end w/ +2 dBm Psat 210 GHz RX front-end 280GHz PAs and LNAs
5/2020 tapeout: Improved 210, 280GHz LNAs and PAs 210 GHz transmitters, receivers using these 2x2 transmitter array with superstrate antenna 2x2 receiver array with superstrate antenna
Seo, UCSB & Sungkyunkwan Univ.; Ahmed, Solyu, Rodwell, UCSB; Li, Zhang, Rebeiz, UCSD
InP IC bonding to patch antenna arrays on quartz. plan: ribbon bonds using wedge bonder
Planned packaging approaches
2x2 array with UCSD SiO2 antenna superstrate simple, expensive in die area limits array size to 2x2 (or 2x4).

## Slide 31: InP ICs for 210GHz Point-Point MIMO
Transceivers & Arrays for 210GHz MIMO links
2/2020 tapeout: 210 GHz TX front-end w/ +20 dBm Psat 210 GHz TX front-end w/ +2 dBm Psat 210 GHz RX front-end 280GHz PAs and LNAs
5/2020 tapeout: Improved 210, 280GHz LNAs and PAs 210 GHz transmitters, receivers using these 2x2 transmitter array with superstrate antenna 2x2 receiver array with superstrate antenna
Seo, UCSB & Sungkyunkwan Univ.; Ahmed, Solyu, Rodwell, UCSB; Li, Zhang, Rebeiz, UCSD
InP IC bonding to patch antenna arrays on quartz. plan: ribbon bonds using wedge bonder
Planned packaging approaches
2x2 array with UCSD SiO2 antenna superstrate simple, expensive in die area limits array size to 2x2 (or 2x4).

## Slide 32: 210 GHz MIMO backhaul: ICs
Transmitter without PA: 
PA 
Receiver:
Transmitter with PA: ✘
Teledyne 250nm (650GHz) InP HBT.
ICs being tested; some to be submitted, others need re-design.
LNA

## Slide 33: 210GHz Power Amplifier
Design goal: high PAE @ 1dB gain compression
Teledyne 250nm InP HBT
A. S. Ahmed, UCSB, results in review

## Slide 34: 300GHz Power Amplifier
Design goal: high PAE @ 1dB gain compression
Teledyne 250nm InP HBT
Measured S-parameters on target
Large-signal (power) data pending.
280GHz design also being tested.
A. S. Ahmed, UCSB

## Slide 35
100-300GHz Wireless

## Slide 36: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-CMOS for short ranges below 200 GHz. SiGe, GaN, or III-V LNAs and PAs for longer-range links. Just like cell phones today SiGe or III-V frequency extenders for 220GHz and beyond
The challenges digital beamformer computational complexity packaging: fitting signal channels in very small areas mesh networking to accommodate beam blockage driving the technologies to low cost

## Slide 37
(backup files follow)