## Slide 1
A Packaged 135GHz 22nm FD-SOI Transmitter on an LTCC Carrier
Ali A. Farid1, Ahmed S. H. Ahmed1,2, Arda Simsek1,3, Mark J. W. Rodwell1
1University of California Santa Barbara, CA, USA
2Marki Microwave Inc., USA, 3Movandi Inc., USA

## Slide 2: Outline
Motivation
Ceramic interposer design/ transition loss
On package Antenna design
Integrated Transmitter module on an LTCC carrier
Link measurement
Conclusion

## Slide 3: Packaging technologies at sub-THz frequencies
IC technologies
Packaging technologies
[Farid et. al.]
[Siwei et. al.]
22FDSOI
45SOI
[Sawaby et. al.]
55nm SiGe
[Ito et. al.]
GaAs HEMT
[Simsek et. al.]
High performance laminate
IL= 2.5dB @140GHz
[Singh et. al.]
Radio on Glass
IL= 1dB @140GHz

## Slide 4: Transmitter IC design
22FDX Chip micrograph
22FDX Chip with Copper pillars
PCB with copper pads
Direct conversation transmitter using GF 22FDSOI
Tx chip is flipchip bonded to LTCC interposer using 50μm diameter copper pillar
Copper pillars are equally spaced at 175μm distance

## Slide 5: Ceramic Interposer design
3 dielectric layers of Kyocera GL771
4 metal layers (ME3 for I/Q routing and LO signal)
How to secure landing copper pillars precisely?
Ceramic coat with 75μm opening
SOP on the ceramic carrier

## Slide 6: CMOS/Interposer transition
Ansys-HFSS
220μm
Simulated transition loss=1.15dB at 135GHz
Transition loss includes
  Copper pillar
  220μm CPW section
Measured transition loss~=0.85dB
Simulated transition loss
measured transition loss

## Slide 7: Series Fed Patch Antenna on LTCC carrier
8-elements series fed patch antenna
transmission line matches antenna to the transmitter 50Ω impedance
Copper pillar transition is part of the impedance matching network

## Slide 8: Measured Antenna performance
11dB gain, 5.5GHz bandwidth
12o E-plane 3-dB beam width
Sidelobes suppressed by 12-dB

## Slide 9: Integrated Transmitter module testing
Tx Input signal swept from 0.1G to 10GHz (either I or Q)
LO signal fixed at 135GHz
Tx upper sideband captured using Harmonic mixer and spectrum analyzer

## Slide 10: Integrated Transmitter module
Module has 6GHz 3-dB modulation BW
Conversion gain=24dB
EIRP at Psat =12.8dB / EIRP at P1dB=8.4dB

## Slide 11: Module Link Measurement
16QAM (6dB-BO) | 
1GBaud | 4GBaud
5.44% RMS | 9.2% RMS
64QAM (8dB-BO) | 
1GBaud | 2GBaud
5.6% RMS | 7.4% RMS
Transmitter (I,Q) data driven by AWG at 2GHz IF
EVM measurements with equalization at DSO.

## Slide 12: Comparison with state of the art
 | Sawaby [SSCL 2018] | Singh [RFIC 2020] | Simsek [RWS2020] | This Work
Package | RO4350 | Radio on Glass | Astra MT77 | LTCC GL771
IC Tech | 55nm SiGe HBT | 0.13μm SiGe-BICMOS | 45nm CMOS SOI | 22nm FDSOI
Antenna Integration | No | No | Yes | Yes
Frequency (GHz) | 110-150 | 115-155 135-170 | 142-147 | 131-137
EIRP at Psat | - | - | 14dBm/ channel | 13dBm
Tx-Psat | -0.5dBm | 13dBm | 2dBm | 1.95dBm
Tx Pdc (mW) | 220 | 1350 2100 | - | 210
Package Loss | 3dB | 1dB | 2.5dB | 0.85~1.1dB
Supported Modulation | QPSK | 256QAM | BPSK | 64QAM

## Slide 13: Conclusion
High performance package with loss transition loss <1dB at 135GHz
Transmitter module has 6GHz 3-dB BW limited by series fed patch antenna BW
EIRP at psat=13dBm (limited by the CMOS TX output power of 2dBm)

## Slide 14: Acknowledge
Kyocera Japan for LTCC carrier fabrication
Kyocera San Diego for module assembly
GF for free access to 22FDX technology and free access to GF advanced copper pillars

## Slide 15
Questions?