## Slide 1
140, 210, and 280GHz IC and transceiver module design
WM1
M. J. W. Rodwell1, U. Soylu1, A. Alizadeh1, S. Lee1, Ali A. Farid1, A. S. H. Ahmed1, M. Seo2, N. Hosseinzadeh1
1University of California, Santa Barbara 2Sungkyunkwan University

## Slide 2: Acknowledgements
Also: Kyocera: D. Kim, H. Horikawa, M. Imayoshi. Samsung: G. Xu, N. Sharma, S. Abu-Surra, W. Choi Pi-Radio: A. Dhananjay, GlobalFoundries: 22nm SOI CMOS ICs

## Slide 3: 100-300GHz Wireless
100-300GHz carriers, massive spatial multiplexing → Terabit hubs and backhaul links, high-resolution imaging radar
Wireless networks: exploding demand.
Immediate industry response: 5G. ~1~40 GHz ("5G?") ~40~100GHz ("5.5G ?") increased spectrum, extensive beamforming
Next generation might be above 100GHz.. (?) greatly increased spectrum, massive spatial multiplexing

## Slide 4: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 5
Applications

## Slide 6: 140GHz Moderate-MIMO hub
If demo uses 32-element array (four 1×8 modules): 16 users/array. P1dB=21 dBm PAs, F=8dB LNAs 1,10 Gb/s/beam→ 16, 160 Gb/s total capacity 70, 40 m range in 50mm/hr rain with 17dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 7: 210 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 2.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 18dBm =P1dB (per element) LNAs: 6dB noise figure

## Slide 8
Systems

## Slide 9: MIMO System Design
ADCs/DACs1: QPSK needs only 3-4 bit ADC/DACs N ADC bits, M antennas, K signals: SNR=6N+1.76+10.log10(M/K) 3 bits, (M/K)=2→ SNR=23 dB. QPSK needs 9.8 dB.
Linearity1: Amplifier P1dB need be only 4 dB above average power
Phase noise2,3: Requirements same as for SISO
Efficient digital beamforming4,5: beamspace algorithm
Efficient VLSI digital beamformer implementation6: low-resolution matrix
Efficient beamforming in broadband arrays7: combined spatial & temporal FFTs.
1) M. Abdelghany et al, IEEE Trans. Wireless Comm, Sept. 2021 2) M. E. Rasekh et al, IEEE Trans. Wireless Comm, Oct. 2021 3) A. Puglielli et al, 2016 IEEE ICC 4) M. Abdelghany, et. al, , 2019 IEEE SPAWC 5) S. H. Mirfarshbafan et al, IEEE Trans CAS 1, 2020 6) O Castañeda Fernández et. al, 2021 ESSCIRC 7) M. Abdelghany et al 2019 IEEE GLOBECOM

## Slide 10
Transistors

## Slide 11: Transistors for 100-300GHz
Results compiled 9/9/2021
CMOS: good power & noise up to ~150GHz. Not much beyond. 65-22nm nodes are best.
InP HBT: record 100-300GHz PAs
SiGe HBT: out-performs CMOS above 200GHz
GaN HEMT: record power below 100GHz. Bandwidth improving
InGaAs-channel HEMT: world's best low-noise amplifiers
Results with low power but high PAE, or low PAE but high power, are not shown

## Slide 12: Summary: InP Transistors & ICs
InP HEMTs: 1.5THz fmax, 1.0THz amplifiers
W. Deal et al, 2016 IEDM (Northrop-Grumman)
130nm InP HBTs: 1.1THz fmax, 3.5V. 670 GHz amplifiers
M. Urteaga, et al, IEEE Proceedings June 2017 (Teledyne)
250nm InP HBTs: 650GHz fmax, 4.5V.
Z. Griffith et al, 2007 IPRM conference (UCSB)
204 GHz static frequency divider Z. Griffith et al, 2010 IEEE CSICS
M. Urteaga, et al, IEEE Proceedings June 2017 (Teledyne)

## Slide 13: 100-300GHz Wireless: Transistor Requirements
Transmitters need: high power-added efficiency high added power density (Pout-Pin)/(gate width, emitter length) Receivers need: low cascaded noise
Need reasonable gain/stage. die area, power, accumulated gain compression
(gain in PAs, LNAs is less than MAG/MSG, U, ... )

## Slide 14: Where the IC designer can't help
mm-wave transistor gain is low: gain-boosting is common Common-source vs. common-gate. Capacitive neutralization. Unconditionally stable positive feedback (Singhakowinta, Int. J. Electronics, 1966) Such circuits don't improve the parameters that matter the most.
The circuit* doesn't change the transistor minimum cascaded noise figure. (Haus, Adler, Proc. IRE, 1958) The circuit* doesn't change the transistor maximum efficiency vs. added power curve.
*If lossless, and given the correct source and load impedances.

## Slide 15
Interconnects

## Slide 16: Normal & Inverted Microstrip
Normal: PAs, LNAs smaller skin-effect losses  ground-plane holes at transistors✘
Inverted: high-density blocks (mixers, phase shifters,…) higher skin-effect losses✘ no ground-plane breaks: better ground integrity
529GHz dynamic divider: M. Seo et al, IEICE Electronics Express, Feb. 2015
266GHz, 16.8dBm PA: A. Ahmed et. al, 2021 IMS

## Slide 17: On-Wafer Interconnect Losses

## Slide 18
Low-Noise Amplifiers

## Slide 19: LNA Design: Noise Close To Transistor Limits
1) Goal: low noise measure, not noise figure
2) Find bias current density for lowest noise measure
@210GHz, Fcascade,min= 6.57 dB given: Je=0.5 mA/um, Vcb=0.3V
3) Minimum M is independent of circuit configuration*; pick for high bandwidth or high gain/stage (= low PDC)
4) Capacitance in common-base; just like inductance in common-emitter, allows simultaneous tuning for zero reflection coefficient and minimum M.
*HA Haus, RB Adler, Proceedings of the IRE, 1958
5) Write ADS Python code to display source impedance for minimum M.
6) Scale transistor size to eliminate series tuning element. Less input tuning→ less noise from passive element loss.
Result: 7.2-7.4dB LNA noise given 6.6dB transistor Fcascade.
<-- all give the same minimum M…
…but common-base gives highest gain (InP HBT @210GHz).
U. Solyu et. al, 2021 EuMIC Conference

## Slide 20
Power Amplifiers

## Slide 21: Current density, finger pitch limit cell output power

## Slide 22: Current density, finger pitch limit cell output power
High Vbr, low Imax ? Device sized to drive 50W might approach lg/4 width. Small finger pitch is critical; limited by thermal design
50W GaN PA cell @ 140GHz (1.6W) 25V swing, 1.67mA/mm, gates: 30 mm width, 15 mm pitch
50W InP HBT PA cell @ 280GHz (40mW) 4V swing, 3.3mA/mm, emitters: 6 mm length, 6 mm pitch
K. Shinohara, Teledyne: GaN HEMT thermal analysis

## Slide 23: Low-Loss 100-300GHz Corporate Combining
Wilkinson trees are lossy: Signal passes through *many* 70.7W, l/4 lines. l/4 lines are long. 70.7W lines are narrow…and lossy→ High loss.
Single-(l/4) combiners are much less lossy Each design uses a single effective l/4 section. Shorter lines, low-Zo lines → lower loss But, low loss only if transistor cells fit.

## Slide 24: 100-300GHz Power combining: what is best ?
Direct series-connected M. Shifrin: 1992 IEEE mWave/mmWave Monolithic Circuits Symp. (Raytheon)
Cascaded combining A. Ahmed 2018 EuMIC, 2021 RFIC (UCSB)
Distributed Active Transformer I. Aoki, IEEE Trans MTT, Jan. 2002 (CalTech)
Balun series-connected l/4 baluns: Y. Yoshihara, 2008 IEEE Asian Solid-State Circuits Conference (Toshiba) sub-l/4 baluns: H. Park, et al, IEEE JSSC, Oct. 2014 (UCSB)
Corporate T-line

## Slide 25: Transistor stacking. Why ? Why not ?
 | Lower frequencies | Higher frequencies
Corporate combining | length → large die area ✘ dB loss → high loss ✘ | length → small die area  dB loss → low loss 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘
 | Lower frequencies | Higher frequencies
Corporate combining |  | 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘

## Slide 26: Series combining using sub-l/4 baluns
81GHz, 17 dB Gain 470 mW Psat , 23% PAE Teledyne 250 nm InP HBT 2 stages, 1.0 mm2(incl pads)
l/4 baluns: Y. Yoshihara, 2008 IEEE Asian Solid-State Circuits Conference (Toshiba) sub-l/4 baluns: H. Park, et al, IEEE JSSC, Oct. 2014 (UCSB)

## Slide 27: Sub-l/4 Balun Combiners. Why ? Why not ?
 | Lower frequencies | Higher frequencies
Corporate combining | length → large die area ✘ dB loss → high loss ✘ | length → small die area  dB loss → low loss 
Sub-l/4 Balun | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘ impedance shift of transistor-balun interconnect ✘
 | Lower frequencies | Higher frequencies
Corporate combining |  | 
Sub-l/4 Balun | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘ impedance shift of transistor-balun interconnect ✘

## Slide 28: Cascade combining as stacking plus matching
A. S. H. Ahmed et al, 2018 EuMIC (UCSB)

## Slide 29: Generalized cascade combining
A. S. H. Ahmed et al, 2018 EuMIC (UCSB) A. S. H. Ahmed, et al, 2021 RFIC Symposium
266GHz, 16.8dBm, 4.0% PAE

## Slide 30: Cascade Combining: Why ? Why not ?
 | Lower frequencies | Higher frequencies
Corporate combining | length → large die area ✘ dB loss → high loss ✘ | length → small die area  dB loss → low loss 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘
Cascade combining | large interstage matching networks✘ | small interstage matching networks  small # transistor fingers per cell → ok  cascade cell pass-though losses ✘
 | Lower frequencies | Higher frequencies
Corporate combining |  | 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘
Cascade combining | large interstage matching networks✘ | small interstage matching networks  small # transistor fingers per cell → ok  cascade cell pass-though losses ✘

## Slide 31: Recent high-efficiency 100-300GHz PAs
130GHz, 200mW, 17.8% PAE
140GHz, 20.5dBm, 20.8% PAE
266GHz, 16.8dBm, 4.0% PAE
194GHz, 17.4dBm, 8.5% PAE
Ahmed et al, 2020 IMS, 2020 EuMIC, 2021 IMS, 2021 RFIC
Teledyne 250nm InP HBT technology

## Slide 32
140 GHz Array Modules

## Slide 33: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 34: Do we need 2D arrays ? 1D steering might be fine.
1/sin2f sidelobes provide strong signals to tall buildings.
Providing sidelobes reduces broadside gain by less than 3dB.
→ Don't need 2D arrays to serve tall buildings

## Slide 35: 2D vs. 1D: user spatial distribution
design 1: 2D array
design 2: 1D array
uniform horizontal & vertical user distributions
uniform horizontal, nonuniform vertical

✘


Spatial distribution of users, and of scattering objects, guides choice of array geometry.

## Slide 36: 140GHz hub: packaging challenges
IC-package interconnects Difficult at > 100 GHz
Removing heat Thermal vias are marginal
Interconnect density Dense wiring for DC, LO, IF, control. Hard to fit these all in.
Economies of scale Advanced packaging standards require sophisticated tools High-volume orders only Hard for small-volume orders (research, universities) Packaging industry is moving offshore

## Slide 37: 100-300GHz IC-package connections

## Slide 38: 140GHz hub: ICs & Antennas
Receiver: A. Farid et. al, 2021 IEEE BCICTS; Transmitter: A. Farid et. al, 2022 IEEE Trans. MTT 10.1109/TMTT.2022.3161972

## Slide 39: 135GHz 8-channel MIMO hub array tile modules
110mW InP PA 20.8% PAE
CMOS TX, RX ICs GlobalFoundries 22nm SOI CMOS.
Teledyne 250nm InP HBT
Receiver: A. Farid et. al, 2021 IEEE BCICTS; Transmitter: A. Farid et. al, 2022 IEEE Trans. MTT 10.1109/TMTT.2022.3161972
140GHz MIMO hub receiver array modules, 4-element, 8-element MIMO beamforming Data transmission up to 1.9Gb/s
140GHz MIMO hub transmitter array modules, 8-element 38.5dBm EIRP Data transmission up to 1.9Gb/s Performance limited by assembly yield. Data rate limited by connector.

## Slide 40
210 GHz and 280 GHz Array Modules

## Slide 41: 210 GHz MIMO backhaul modules
8-element MIMO array 3.1 m baseline for 500m link. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 63mW =P1dB (per element) LNAs: 6dB noise figure

## Slide 42: 210 GHz Transmitter and Receiver ICs
M. Seo et al, 2021 IMS; Teledyne 250nm InP HBT
Size: 2.3 x 0.85 mm2
Size: 2.9 x 0.75 mm2

## Slide 43: 200 GHz MIMO backhaul modules
1-channel modules w/ 200 GHz InP 1-channel Tx, Rx ICs (simplicity)
2x2 patch antenna feed on fused silica substrate
200 mm Teflon lens
Assembly: 200 GHz ribbon bonds, low-frequency ball-bonds
280 GHz modules will be similar

## Slide 44: 200 GHz MIMO backhaul modules

## Slide 45
Seo, Sungkyunkwan Univ. & UCSB; Soylu, Ahmed, Rodwell, UCSB; Li, Zhang, Rebeiz, UCSD
200 GHz 2x2 transmitter & receiver arrays
2 x 2 Phased-array transmitter and receiver: same IC design as single-channel transceivers, LO phase-shift beamforming: broadband, patch antennas on quartz superstrate.
Modules being assembled for testing.

## Slide 46: 280GHz Transmitter and Receiver ICs
Rodwell, UCSB
Teledyne 250nm InP HBT technology.
Transmitter (simulated): 17dBm saturated output power ~40GHz bandwidth,
Receiver (simulated): 12dB noise figure 40GHz bandwidth
Objective: 80Gb/sec/channel for MIMO backhaul demonstration.
2nd-Gen Designed Taped out March 2022.
Receiver
Transmitter
Solyu, Alizadeh, Rodwell, UCSB, Seo, Sungkyunkwan Univ.

## Slide 47
100-300GHz Wireless

## Slide 48: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-silicon for short ranges below 200 GHz. SiGe or III-V LNAs and PAs for longer-range links. Just like cell phones today III-V frequency extenders for 340GHz and beyond
The challenges computational complexity packaging: fitting signal channels in very small areas mesh networking to accommodate beam blockage driving the technologies to low cost

## Slide 49
In case of questions

## Slide 50: 70 GHz spatially multiplexed base station
If we use instead a 70GHz carrier, the range increases to 70 meters (vs. 40 meters) but the handset becomes 16mm×16mm (vs. 8mm×8mm), and the hub array becomes 19mm×612mm (vs. 10mm×328mm)
Or, use a 4×4 (8mm×8mm) handset array, and the range becomes ..about 40 meters.
Same handset area (more handset elements)→ same link budget Easier to obtain license for 140±2.5GHz than 70±2.5GHz

## Slide 51: 75 GHz, 640 Gb/s MIMO backhaul (16QAM)
Why not use a lower-frequency carrier, e.g. 75 GHz ? Must use at least 16QAM, given 80Gb/s/channel…
Similar RF power output, physically larger
8-element 640Gb/s linear array:
requires 16dBm transmit power/element (Pout)
requires 3.5m linear array

## Slide 52: References
Systems Design
100-300GHz Link examples: M. J. W. Rodwell, "100-340GHz Spatially Multiplexed Communications: IC, Transceiver, and Link Design," 2019 IEEE 20th International Workshop on Signal Processing Advances in Wireless Communications (SPAWC), 2019, pp. 1-5, doi: 10.1109/SPAWC.2019.8815433.
Required ADC/DAC resolution and amplifier IP3, P1dB in massive MIMO: M. Abdelghany, A. A. Farid, M. E. Rasekh, U. Madhow and M. J. W. Rodwell, "A Design Framework for All-Digital mmWave Massive MIMO With per-Antenna Nonlinearities," in IEEE Transactions on Wireless Communications, vol. 20, no. 9, pp. 5689-5701, Sept. 2021, doi: 10.1109/TWC.2021.3069378.
Phase noise in massive MIMO: M. E. Rasekh, M. Abdelghany, U. Madhow and M. Rodwell, "Phase Noise in Modular Millimeter Wave Massive MIMO," in IEEE Transactions on Wireless Communications, vol. 20, no. 10, pp. 6522-6535, Oct. 2021, doi: 10.1109/TWC.2021.3074911.
Phase noise in massive MIMO: A. Puglielli, G. LaCaille, A. M. Niknejad, G. Wright, B. Nikolić and E. Alon, "Phase noise scaling and tracking in OFDM multi-user beamforming arrays," 2016 IEEE International Conference on Communications (ICC), 2016, pp. 1-6, doi: 10.1109/ICC.2016.7511631.
Beamspace algorithm for MIMO hub digital beamforming: M. Abdelghany, U. Madhow and A. Tölli, "Beamspace Local LMMSE: An Efficient Digital Backend for mmWave Massive MIMO," 2019 IEEE 20th International Workshop on Signal Processing Advances in Wireless Communications (SPAWC), 2019, pp. 1-5, doi: 10.1109/SPAWC.2019.8815585.
Beamspace algorithm and VLSI design for MIMO hub digital beamforming: S. H. Mirfarshbafan, A. Gallyas-Sanhueza, R. Ghods and C. Studer, "Beamspace Channel Estimation for Massive MIMO mmWave Systems: Algorithm and VLSI Design," in IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 67, no. 12, pp. 5482-5495, Dec. 2020, doi: 10.1109/TCSI.2020.3023023.
Digital beamformer IC: Oscar F. Castaneda Fernandez , Zachariah Boynton , Seyed Hadi Mirfarshbafan , Shimin Huang , Jamie Ye , Alyosha Molnar , Christoph Studer, "A Resolution-Adaptive 8mm2 9.98Gb/s 39.7pJ/b 32-Antenna All-Digital Spatial Equalizer for mmWave Massive MU-MIMO in 65nm CMOS", 2021 European Solid-State Circuits Conference.
Algorithms for MIMO digital beamforming with broaband waveforms: M. Abdelghany, U. Madhow and M. Rodwell, "An Efficient Digital Backend for Wideband Single-Carrier mmWave Massive MIMO," 2019 IEEE Global Communications Conference (GLOBECOM), 2019, pp. 1-6, doi: 10.1109/GLOBECOM38437.2019.9013233.

## Slide 53: References
Transistors
InP HEMT:W. R. Deal, K. Leong, W. Yoshida, A. Zamora and X. B. Mei, "InP HEMT integrated circuits operating above 1,000 GHz," 2016 IEEE International Electron Devices Meeting (IEDM), 2016, pp. 29.1.1-29.1.4, doi: 10.1109/IEDM.2016.7838502
InP HBT: M. Urteaga, Z. Griffith, M. Seo, J. Hacker and M. J. W. Rodwell, "InP HBT Technologies for THz Integrated Circuits," Proceedings of the IEEE, vol. 105, no. 6, pp. 1051-1067, June 2017, doi: 10.1109/JPROC.2017.2692178.
InP HBT: M. J. W. Rodwell, M. Le and B. Brar, "InP Bipolar ICs: Scaling Roadmaps, Frequency Limits, Manufacturable Technologies," in Proceedings of the IEEE, vol. 96, no. 2, pp. 271-286, Feb. 2008, doi: 10.1109/JPROC.2007.911058.
finFET: H. Lee, S. Callender, S. Rami, W. Shin, Q. Yu and J. M. Marulanda, "Intel 22nm Low-Power FinFET (22FFL) Process Technology for 5G and Beyond," 2020 IEEE Custom Integrated Circuits Conference (CICC), 2020, pp. 1-7, doi: 10.1109/CICC48029.2020.9075914.
22nm SOI CMOS: C. Li et al., "5G mm-Wave front-end-module design with advanced SOI process," 2017 IEEE 12th International Conference on ASIC (ASICON), 2017, pp. 1017-1020, doi: 10.1109/ASICON.2017.8252651.
SiGe HBT: B. Heinemann et al., "SiGe HBT with ft/fmax of 505 GHz/720 GHz," 2016 IEDM, San Francisco, CA, 2016, pp. 3.1.1-3.1.4.
GaN HEMT: S. Wienecke et al., "N-Polar GaN Cap MISHEMT With Record Power Density Exceeding 6.5 W/mm at 94 GHz," IEEE Electron Device Letters, vol. 38, no. 3, pp. 359-362, March 2017
GaN HEMT: A. Fung et al., "Gallium nitride amplifiers beyond W-band," 2018 IEEE Radio and Wireless Symposium (RWS), 2018, pp. 150-153, doi: 10.1109/RWS.2018.8304971.

## Slide 54: References
Power Amplifiers
Stacking: M. Shifrin, Y. Ayasli, and P. Katzin, “A new power amplifier topology with series biasing and power combining of transistors,” in 1992 IEEE Microwave and Millimeter-Wave Monolithic Circuits Symp. Dig. Papers, Jun. 1992, pp. 39–41.
Stacking: S. Pornpromlikit, H.-T. Dabag, B. Hanafi, J. Kim, L. Larson, J. Buckwalter, and P. Asbeck, “A Q-band amplifier implemented with stacked 45-nm CMOS FETs,” in Proc. 2011 IEEE Compound Semiconductor Integrated Circuit Symp. (CSICS), Oct. 2011, pp. 1–4.
Distributed active transformers: I. Aoki, S. Kee, D. Rutledge, and A. Hajimiri, “Distributed active transformer: A new power-combining and impedance-transformation technique,” IEEE Trans. Microw. Theory Tech., vol. 50, no. 1, pp. 316–331, Jan. 2002S
Series combining with baluns: Y. Yoshihara, R. Fujimoto, N. Ono, T. Mitomo, H. Hoshino and M. Hamada, "A 60-GHz CMOS power amplifier with Marchand balun-based parallel power combiner," 2008 IEEE Asian Solid-State Circuits Conference, 2008, pp. 121-124, doi: 10.1109/ASSCC.2008.4708744.
Series combining with sub-quarter-wave baluns: H. Park, S. Daneshgar, Z. Griffith, M. Urteaga, B. Kim and M. Rodwell, "Millimeter-Wave Series Power Combining Using Sub-Quarter-Wavelength Baluns," IEEE JSSC, vol. 49, no. 10, pp. 2089-2102, Oct. 2014
Cascade combining: A. S. H. Ahmed, A. A. Farid, M. Urteaga and M. J. W. Rodwell, "204GHz Stacked-Power Amplifiers Designed by a Novel Two-Port Technique," 2018 13th European Microwave Integrated Circuits Conference (EuMIC), 2018, pp. 29-32, doi: 10.23919/EuMIC.2018.8539884.
270GHz InP HBT PA: A. S. H. Ahmed, U. Soylu, M. Seo, M. Urteaga and M. J. W. Rodwell, "A compact H-band Power Amplifier with High Output Power," 2021 IEEE Radio Frequency Integrated Circuits Symposium (RFIC), 2021, pp. 123-126, doi: 10.1109/RFIC51843.2021.9490426.
140GHz CMOS PA: S. Li and G. M. Rebeiz, "A 130-151 GHz 8-Way Power Amplifier with 16.8-17.5 dBm Psat and 11.7-13.4% PAE Using CMOS 45nm RFSOI," 2021 IEEE Radio Frequency Integrated Circuits Symposium (RFIC), 2021, pp. 115-118, doi: 10.1109/RFIC51843.2021.9490507.

## Slide 55: References
Power Amplifiers (more)
270GHz power amplifier: A. S. H. Ahmed, U. Soylu, M. Seo, M. Urteaga and M. J. W. Rodwell, "A compact H-band Power Amplifier with High Output Power," 2021 IEEE Radio Frequency Integrated Circuits Symposium (RFIC), 2021, pp. 123-126, doi: 10.1109/RFIC51843.2021.9490426.
200GHz power amplifier: A. S. H. Ahmed, U. Soylu, M. Seo, M. Urteaga, M. J. W. Rodwell, "A 190-210GHz Power Amplifier with 17.7-18.5dBm Output Power and 6.9-8.5% PAE." IEEE International Microwave Symposium (IMS). 6-11 June, Atlanta and virtual
130GHz power amplifier: A. S. H. Ahmed, M. Seo, A. A. Farid, M. Urteaga, J. F. Buckwalter and M. J. W. Rodwell, "A 200mW D-band Power Amplifier with 17.8% PAE in 250-nm InP HBT Technology," 2020 15th European Microwave Integrated Circuits Conference (EuMIC), 2021, pp. 1-4, doi: 10.1109/EuMIC48047.2021.00012.
140GHz power amplifier: A. S. H. Ahmed, M. Seo, A. A. Farid, M. Urteaga, J. F. Buckwalter and M. J. W. Rodwell, "A 140GHz power amplifier with 20.5dBm output power and 20.8% PAE in 250-nm InP HBT technology," 2020 IEEE/MTT-S International Microwave Symposium (IMS), 2020, pp. 492-495, doi: 10.1109/IMS30576.2020.9224012.
LNAs
200GHz InP HBT LNAs: Utku Soylu, Ahmed S. H. Ahmed, Munkyo Seo, Ali Farid, Mark Rodwell, "200 GHz Low Noise Amplifiers in 250nm InP HBT Technology", 2021 EuMIC (delayed by COVID to Jan 2022 )
InGaAs-channel HEMT LNAs: G. Moschetti et al., "A 183 GHz Metamorphic HEMT Low-Noise Amplifier With 3.5 dB Noise Figure," in IEEE Microwave and Wireless Components Letters, vol. 25, no. 9, pp. 618-620, Sept. 2015, doi: 10.1109/LMWC.2015.2451355.
Circuit theory
Maximum acheivable unconditionally stable gain: A. Slnghakowinta & A. R. Boothroyd (1966) Gain Capability of Two-port Amplifiers , International Journal of Electronics, 21:6, 549-560, DOI: 10.1080/00207216608937931
Noise theory: H. A. Haus and R. B. Adler, "Optimum Noise Performance of Linear Amplifiers," in Proceedings of the IRE, vol. 46, no. 8, pp. 1517-1533, Aug. 1958. doi: 10.1109/JRPROC.1958.286973

## Slide 56: References
Frequency Dividers
Static Dividers: Z. Griffith, M. Urteaga, R. Pierson, P. Rowell, M. Rodwell and B. Brar, "A 204.8GHz Static Divide-by-8 Frequency Divider in 250nm InP HBT," 2010 IEEE Compound Semiconductor Integrated Circuit Symposium (CSICS), 2010, pp. 1-4, doi: 10.1109/CSICS.2010.5619684.
Dynamic Dividers: Munkyo Seo, John Hacker, Miguel Urteaga, Anders Skalare, Mark Rodwell, " A 529 GHz Dynamic Frequency Divider in 130 nm InP HBT Process", IEICE Electronics Express, Vol. 12 (2015) No. 3 pp. 20141118. February 10, 2015, https://doi.org/10.1587/elex.12.20141118
Phased arrays and MIMO Transeiver modules
CMOS phased array: S. Li, Z. Zhang, B. Rupakula and G. M. Rebeiz, "An Eight-Element 140-GHz Wafer-Scale IF Beamforming Phased-Array Receiver With 64-QAM Operation in CMOS RFSOI," in IEEE Journal of Solid-State Circuits, doi: 10.1109/JSSC.2021.3102876.
CMOS phased array: Siwei Li, Zhe Zhang , Bhaskara R. Rupakula, Gabriel M. Rebeiz, "An Eight-Element 140 GHz Wafer-Scale Phased-Array Transmitter with 32 dBm Peak EIRP and > 16 Gbps 16QAM and 64QAM Operation", 2021 IEEE MTT-S International Microwave Symposium
140GHz CMOS MIMO receiver hub modules: A. A. Farid, A. S. H. Ahmed, A Dhananjay, P. Skrimponis, S. Rangan, M. J. W. Rodwell, "135GHz CMOS / LTCC MIMO Receiver Array Tile Modules", 2021 IEEE BiCMOS and Compound Semiconductor Integrated Circuits and Technology Symposium (BCICTS),
140GHz CMOS MIMO receiver and transmitter hub modules: Ali A. Farid, Ahmed S. H. Ahmed, Aditya Dhananjay, Mark J. W. Rodwell, "135GHz Transmitter and Receiver Multiuser MIMO Array Tiles for Wireless Communications", submitted to IEEE JSSC.
M. Seo, A. S. H. Ahmed, U. Soylu, A. Farid, Y. Na and M. Rodwell, "A 200 GHz InP HBT Direct-Conversion LO-Phase-Shifted Transmitter/Receiver with 15 dBm Output Power," 2021 IEEE MTT-S International Microwave Symposium (IMS), 2021, pp. 378-381, doi: 10.1109/IMS19712.2021.9575035.