## Slide 1
Paper 2b.2
  A 280 GHz (x8) Frequency Multiplier Chain
  in 250 nm InP HBT Technology
Utku Soylu1
Amirreza Alizadeh1, Munkyo Seo2, Mark J. W. Rodwell1
1ECE, University of California, Santa Barbara, USA
2ECE, Sungkyunkwan University, South Korea
Notes: The slide guide is meant to be used with PowerPoint.

## Slide 2: 200-300 GHz Wireless Backhaul
Growing demand for wireless communications: endpoint and backhaul 200-300 GHz backhaul: 100+ Gb/s feasible over ~km range. → develop 200-300 GHz transceivers
Notes: Please follow the allowed time so the program runs on schedule

## Slide 3: mm-wave LO generation
PLLs: in-band phase noise: N2×reference (plus additive noise) out-of-band phase noise: VCO challenge: low-noise mm-wave VCO Multipliers: phase noise: N2×reference (plus additive noise)
spurious harmonics: out-of-band response
Notes: Please follow the allowed time so the program runs on schedule

## Slide 4: Push-Push Frequency Doubler
Push-push: odd harmonic suppression. Maximum Pout design: voltage swing between Vce,sat and Vbr,ceo. Here: loadline instead tuned for maximum PAE (smaller Vmax).
Notes: Please follow the allowed time so the program runs on schedule

## Slide 5: Doubler: Voltage vs. Current Bias
Voltage bias: output current & charge increase with Pin.
Current bias: output charge independent of Pin. → less variation of Pout with Pin.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 6: Teledyne 250 nm InP HBT
fmax = 650 GHz.
Jmax = 3 mA/µm.
BVCEo= 4.5 V.
Four interconnect levels
Microstrip lines (M4 signal, M1 ground) 1.0 dB/mm @ 280 GHz
Resistors: 50 Ω/square
MIM capacitors: 0.3 fF/µm2
Notes: Please follow the allowed time so the program runs on schedule

## Slide 7: Doubler Area Scaling/Bias Condition
Pout, dBm
Pin, dBm
Gain, dB
HBT emitter length set such that Pout > Pin.
→ Cascaded doublers don't need inter-stage amplifiers .
Notes: Please follow the allowed time so the program runs on schedule

## Slide 8: Input/Output Matching
Transistor Current, mA
Transistor Output Voltage, V
140 GHz input tuning: 50 Ω large-signal match
280 GHz output (50 Ω load): current swing at HBT safe limits (2.3 mA/mm) voltage swing below HBT (VBRCEO-VCE,sat) limits: less saturated ouput power but greater gain.
Emitter RC network improves low-frequency common-mode stability.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 9: Single-ended to Differential Conversion
CMRR, dB
Freq, GHz
0.5 dB loss at 140 GHz.
Simulated phase imbalance: 10o & Simulated amplitude imbalance: 0.2 dB
Single-ended input to differential output amplifier with high CMRR:
Better spurious harmonic rejection at the expense of DC power consumption.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 10: x8 Frequency Multiplier Chain
280GHz Pin = -2 dBm | 0.25um x 6um, 3 cascaded x2
Multiplication | x8
BW3dB | 48 GHz
Pout | -0.6 dBm
PDC | 112 mW
Die Area | 0.4 mm2
Spurious Harmonic Suppression | 28 dBc
Notes: Please follow the allowed time so the program runs on schedule

## Slide 11: Power Measurement Setup
Simultaneous power and spectrum measurement.
Spurious-free tone to calculate cross-calibration coefficient generated by FMC.
High-order passive harmonic mixer limits minimum detectable signal power.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 12: Measurement Results: Pout vs Pin
Pin = -1.2 dBm → Pout(@7th harmonic) = -31 dBm
Pin = 3.3 dBm → Pout(@9th harmonic) = -28.3 dBm
280 GHz
Notes: Please follow the allowed time so the program runs on schedule

## Slide 13: Measurement Results: Pout vs Pin
Pin = 0 dBm:
280 GHz: Measured Pout : -0.8 dBm, Simulated Pout : 0.9 dBm
300 GHz: Measured Pout : -3.3 dBm, Simulated Pout : -0.3 dBm
Inaccurate large-signal device modelling at high frequencies.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 14: Measurement Results: Pout vs freq
Pin = -2 dBm → 2 dBm:
3-dB bandwidth: 48 GHz → 60 GHz.
Harmonic suppression: 28 dBc → 20 dBc
Set Pin for high spectral purity or wider operating bandwidth.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 15: Measurement Results: Output Spectrum
Pin = -6 dBm: Spurious harmonics are below the noise floor.
Low order/fundamental mixer → better dynamic range.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 16: Transmitter/Receiver with x8 FMC
280 GHz direct-conversion RX
280 GHz direct-conversion TX
Notes: Please follow the allowed time so the program runs on schedule

## Slide 17: Performance Comparison
This work shows record spectral purity among H-band frequency multipliers.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 18: Acknowledgement
This work was supported by ComSenTer, a JUMP program sponsored by the Semiconductor Research Corporation.
The authors thank Teledyne Scientific & Imaging for the IC fabrication.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 19
THANK YOU
Notes: Please follow the allowed time so the program runs on schedule

## Slide 20: References
M. J. W. Rodwell et al., "100-300GHz Wireless: ICs, Arrays, and Systems," 2021 IEEE BiCMOS and Compound Semiconductor Integrated Circuits and Technology Symposium (BCICTS), 2021, pp. 1-4.
E. Turkmen, I. K. Aksoyak, W. Debski, W. Winkler and A. Çaǧri Ulusoy, "A 220-261 GHz Frequency Multiplier Chain (x18) With 8-dBm Peak Output Power in 130-nm SiGe," in IEEE Microwave and Wireless Components Letters.
M. Bao, T. N. Thi Do, D. Kuylenstierna and H. Zirath, "A 135–183GHz Frequency Sixtupler in 250nm InP HBT," 2020 IEEE/MTT-S International Microwave Symposium (IMS), 2020, pp. 480-483.
T. Buecher, S. Malz, K. Aufinger and U. R. Pfeiffer, "A 210–291-GHz (8×) Frequency Multiplier Chain With Low Power Consumption in 0.13-μm SiGe," in IEEE Microwave and Wireless Components Letters, vol. 30, no. 5, pp. 512-515, May 2020.
U. J. Lewark, A. Tessmann, S. Wagner, A. Leuther, T. Zwick and I. Kallfass, "A 220 to 320 GHz broadband active frequency multiplier-by-eight MMIC," 2014 9th European Microwave Integrated Circuit Conference, 2014, pp. 132-135.
J. Yu, J. Chen, Z. Li, D. Hou, Z. Chen and W. Hong, "A 212–260 GHz Broadband Frequency Multiplier Chain (×4) in 130-nm BiCMOS Technology," 2021 IEEE MTT-S International Microwave Symposium (IMS), 2021, pp. 454-457.
K. Lee, H. Hamada, H. Matsuzaki, H. Nosaka and H. -J. Song, "220 – 265 GHz Active x6 Frequency Multiplier MMIC with InP HEMT Technology," 2018 IEEE/MTT-S International Microwave Symposium - IMS, 2018, pp. 765-768.
N. Sarmah, B. Heinemann and U. R. Pfeiffer, "235–275 GHz (x16) frequency multiplier chains with up to 0 dBm peak output power and low DC power consumption," 2014 IEEE Radio Frequency Integrated Circuits Symposium, 2014, pp.
K. Katayama, K. Takano, S. Amakawa, T. Yoshida and M. Fujishima, "2.37-dBm-output 288–310 GHz frequency multiplier in 40 nm CMOS," 2017 IEEE International Symposium on Radio-Frequency Integration Technology (RFIT), 2017, pp. 28-30.
A. Ali, J. Yun, M. Kucharski, H. J. Ng, D. Kissinger and P. Colantonio, "220–360-GHz Broadband Frequency Multiplier Chains (x8) in 130-nm BiCMOS Technology," in IEEE Transactions on Microwave Theory and Techniques, vol. 68, no. 7, pp. 2701-2715, July 2020.
M. Urteaga, et al., “InP HBT Technologies for THz Integrated Circuits”, Proc. of the IEEE, vol. 105, no. 6, pp 1051-1067, June 2017.
Juo-Jung Hung, T. M. Hancock and G. M. Rebeiz, "High-power high-efficiency SiGe Ku- and Ka-band balanced frequency doublers," in IEEE Transactions on Microwave Theory and Techniques, vol. 53, no. 2, pp. 754-761, Feb. 2005.
A. S. H. Ahmed, U. Soylu, M. Seo, M. Urteaga and M. J. W. Rodwell, "A compact H-band Power Amplifier with High Output Power," 2021 IEEE Radio Frequency Integrated Circuits Symposium (RFIC), 2021, pp. 123-126.
Notes: Please follow the allowed time so the program runs on schedule

## Slide 21: Power Measurement Setup (Pictures)
Notes: Please follow the allowed time so the program runs on schedule