## Slide 1
(Paper 9b.2)
10/18/2023
D-Band Power Amplifier with 27 dBm Peak Output Power and 14.9% PAE in 250-nm InP HBT Technology
Amirreza Alizadeh1, Utku Soylu1, Navneet Sharma2, Gary Xu2, Mark J. W. Rodwell1
1University of California, Santa Barbara, USA
2Samsung Research America, Plano, TX, USA
rodwell@ucsb.edu
Notes: The slide guide is meant to be used with PowerPoint.

## Slide 2: 100-300 GHz Wireless
High capacity: potentially wide available bandwidth massive spatial multiplexing even with compact arrays
Limited range: high l2/R2 path losses high worst-case atmospheric attenuation
Need: arrays with many elements low receiver noise figure compact, efficient, 100-300 GHz power amplifiers
140 GHz MIMO Hub
Abu-Surra, Samsung/UCSB 2022 IEEE ICC
200 GHz backhaul
Soylu, UCSB 2023 IEEE BCICTS

## Slide 3: Technology Comparison: 100-220 GHz PAs
110-200 GHz: InP HBT provides leading output power vs. efficiency
200-300 GHz: InP HBT and InP HEMT are both excellent
Results compiled 8/16/2023

## Slide 4: Teledyne 250 nm InP HBT Technology
HBTs: ~200-400 GHz ft; varies with Vce, Ic
~650 GHz fmax
~3 mA/mm maximum current
~4.5 V breakdown
~0.6 V minimum at 2mA/mm (Kirk effect)
Griffith, 2007 IEEE IPRM Urteaga, 2017 IEEE Proceedings
Back end: 4 Au wiring layers, BCB dielectric (er=2.65) 5 mm M1-M4 separation→ ~0.9 dB/mm loss @ 140 GHz
MIM capacitors: 0.3 fF/mm2
Thin-film resistors: 50 W/square

## Slide 5: 500 mW, 150 GHz PA Design Challenges
Overheating (~3 W dissipation): minimum output transistor power cell spacing, IC bonded to metal heat sink
~1 Amp DC supply currents: electromigration, I2R losses→ wide conductors
Efficiency: minimize tuning & power-combining losses
Electrothermal self-destruction: power cell ballasting
Efficient class-AB operation: electrothermally stable adaptive bias circuits

## Slide 6: Capacitively Degenerated Common-Base
Common-base with AC grounded base : more small-signal gain than common-emitter
Capacitively degenerated common base finite base capacitance smaller gain, same peak PAE at same (Pout-Pin)
less gain compression @ peak PAE. broadband stability with no loss in PAE
Power from previous stages contributes to Pout. …similar to stacking
4x 6 mm HBT cell; no cell parasitics

## Slide 7: Bipolar Transistor Electrothermal Runaway
W. Liu, IEEE TED, March 1996

## Slide 8: Class-B biasing of HBT power amplifiers

## Slide 9: Power detectors & peak detectors

## Slide 10: Common-base class-AB adaptive bias circuit
Low-power operation: current Iref produces voltage across R2. → produces equal voltage across R1 → forces base current Ib1, produces collector current Ic1 Ic1 is independent of ambient temperature
High power operation Vbe1,DC and Vb2,DC both decrease by (Vin,RF,peak)2/4Vt. → increases the voltage drop across R1. → increases Ib1,DC , Ic1,DC Ic1,DC varies as k1+k2PRF ; increases with RF power
Why two rectifying elements ? doubles the rectified DC voltage. R1 can be 2:1 larger for a given variation of Ic1,DC with PRF . → increases electrothermal stability factor.
Adaptive bias also reduces gain variation vs. output power.
Q1: RF gain; Q2: DC bias.

## Slide 11: High-power D-band class-AB amplifier
ABN = Active Bias Network ISMN = Inter-stage Matching Network IMN = Input Matching Network ONM= Output Matching Network Simulated bias currents shown at peak RF power.

## Slide 12: die photo
2 mm x 1.5 mm: designed to fit in 140 GHz linear array
1 active bias network for each 4-finger HBT
Each bias network is very close to
the HBT being biased.

## Slide 13: Measured Small-Signal Parameters
Vcc=2.4 V: ~20 dB midband gain 119–162 GHz bandwidth (-3 dB)
As Vcc increases:
→ more PDC (more IC, more VCE) → more heating → decreased gain S21 .
Bias currents will be greater under high-power operation.

## Slide 14: Power Measurements
Amplifier overloads power meter Add 40 cm waveguide attenuator Calibration: s=0.33 dB (6 repeated measurements)
Amplifier output power measurement IC bonded with high-Kth adhesive to Cu heat sink
Determining probe losses: Measure loss of probe/line/probe (negligible line loss) Weaknesses: division by 2, on-wafer structures near DUT variability estimate: s=1 dB (typical of D-band power data)
To be conservative, focus on 150 GHz data, where probe loss correction is smallest (2.24 dB)

## Slide 15: 150 GHz Power Characteristics
14.9% peak PAE
27.2 dBm output power at peak PAE

## Slide 16: 125-155 GHz Power Characteristics
Pout > 26 dBm over 126-150 GHz

## Slide 17: Adaptive Bias Circuit Operation: 138 GHz
IC shows expected
linear variation of bias currents vs. RF power

## Slide 18: High-Power InP D-band Amplifier
Record 27 dBm output power at 150 GHz; 14.9% associated PAE
> 26 dBm over 126-150 GHz
2 mm x 1.5 mm die; fits in 140 GHz, 0.6l-pitch linear array
Teledyne 250 nm InP HBT technology.
Adaptive bias circuits: class-AB bias, electrothermal stabilization.
4x 6 mm HBT cell; no cell parasitics

## Slide 19: Questions ?
adaptive class-AB bias
2 mm x 1.5 mm

## Slide 20: backup slides

## Slide 21: Capacitive Degeneration: Optimum Gain
Capacitive degeneration: no effect on peak PAE….given lossless embedding No capacitive degeneration: more gain compression @ P1dB. ✘ more gain @ P1dB  input matching losses have less effect on PAE 
With capacitive degeneration: less gain compression @ P1dB.  less gain @ P1dB ✘ input matching losses have more effect on PAE ✘
Design for greatest PAE @ P1dB balances these two considerations.
4x 6 mm HBT cell; no cell parasitics