## Slide 1
WSQ-4
ICs and Transceivers for 100–300 GHz Wireless
With acknowledgements to
U. Soylu1,2, A. Alizadeh1,3, A. S. S. Ahmed1,4, A. Farid1,5, M. Urteaga6, M. Seo7, K. Park1, C. Seo1, Y. Nemoto1, E. C. Bormali1
1University of California, Santa Barbara 2Now with IBM Yorktown 3Now with Keysight Technologies 4Now with Cairo University 5Now with Intel 6Teledyne Scientific 7Sungkyunkwan University
Mark J. W. Rodwell, Doluca Family Chair, University of California, Santa Barbara

## Slide 2: 100-300 GHz Wireless
High capacity: potentially wide available bandwidth massive spatial multiplexing even with compact arrays
Limited range: high l2/R2 path losses high worst-case atmospheric attenuation
Need: arrays with elements low receiver noise figure compact, efficient, medium-power amplifiers
Nomenclature: 30-300 GHz = 10 mm to 1 mm wavelengths * millimeter-waves *

## Slide 3: High-Capacity Radio Links

## Slide 4: Concept: 640 Gb/s, 140 GHz MIMO hub
Concept 64 beams at 10 Gb/s/beam 128 antennas, each (9l x l/2) 70 meters range in 50 mm/hr. rain 17 dB margins: (obstruction, operating, aging, packaging) LNAs: 8 dB noise figure PAs : 100 mW =P1dB (per element)
Actual demos (with Samsung, Pi-Radio) 8-element arrays
Farid: 2021 IEEE BCICTS Farid: 2022 IEEE Trans MTT Abu-Surra : 2022 IEEE ICC
Kyocera: LTCC interposers. Globalfoundries 22FDX SOI CMOS Teledyne 250 nm InP HBT

## Slide 5: 70 m, 64 × 10 Gb/s hub: 140, 70, 35 GHz
High frequencies are advantageous if aR < 1.
Frequency |  | 140 GHz | 70 GHz |  | 35 GHz | 
Handset | size | 9 mm x 9 mm | 9 mm x 9 mm |  | 9 mm x 9 mm | 
 | # elements | 8 x 8 | 4 x 4 |  | 2 x 2 | 
Hub | size | 13 cm x 1.0 cm | 26 cm x 2.0 cm |  | 52 cm x 4.0 cm | 
 | # elements | 128 x 1 | 128 x 1 |  | 128 x 1 | 
Modulation |  | QPSK | QPSK | 16QAM | QPSK | 64QAM
Channel Bandwidth |  | 5 GHz | 5 GHz | 2.5 GHz | 5 GHz | 1.7 GHz
Transmit P1dB /element |  | 20.1 dBm | 20.1 dBm | 24.2 dBm | 19.5 dBm | 27.8 dBm
 | high capacity | moderate capacity
long range | ----- | moderate frequency
short range | high frequency | moderate frequency
Assumptions: Hub to handset downlink. Link parameters as per previous slide. Same range, noise figure, rain rate, margins.

## Slide 6: Concept: 640 Gb/s, 210 GHz MIMO backhaul
Concept 8x 80 Gb/s MIMO with 2.1 m baseline 16-element subarrays (7l x 7l antennas) 500 meters range in 50 mm/hr. rain 14 dB margins: (obstruction, operating, aging, packaging) LNAs: 8 dB noise figure
PAs: 50 mW =P1dB
Demonstrated to date: no subarrays, 1 channel
Ongoing demonstration efforts: no subarrays, 4 x 4 MIMO

## Slide 7: 500 m, 640 Gb/s backhaul: 280, 140, 90, 35 GHz
Frequency |  | 280 GHz | 140 GHz | 90 GHz |  | 35 GHz | 
1 x 8 MIMO array length, L |  | 1.8 m | 2.6 m | 3.2 m |  | 5.1 m | 
subarrays | size | 3.1 x 3.1 cm2 | 6.2 x 6.2 cm2 | 9.5 x 9.5 cm2 |  | 25 x 25 cm2 | 
 | # elements | 4 x 4 | 4 x 4 | 4 x 4 |  | 4 x 4 | 
Modulation |  | QPSK | 16QAM | 16QAM | 64QAM | 64QAM | 4096QAM
Channel Bandwidth |  | 40 GHz | 20 GHz | 20 GHz | 13 GHz | 13 GHz | 6.7 GHz
Transmit P1dB/element |  | 19.7 dBm | 16.1 dBm | 12.3 dBm | 16.5 dBm | 4.1 dBm | 19.2 dBm
Assumptions: Link parameters as per previous slide. All carrier frequencies analyzed with same range, transmit power/element, noise figure, rain rate, margins.
High frequencies are advantageous if aR < 1.
 | high capacity | moderate capacity
long range | ----- | moderate frequency
short range | high frequency | moderate frequency

## Slide 8: Radio link design: Implications
Worst-case atmospheric losses similar at 50 GHz & 200 GHz
Same link budgets, if # array elements are moderately increased @ 200 GHz If comparable PA and LNA performance can be obtained. → work on LNAs, PAs, work on realizing much larger arrays
But, any terrestrial > 50 GHz system will be short-range.

## Slide 9: 100-300 GHz Wireless ?? Even 39 GHz is hard !
Viable 100-300 GHz wireless systems need: acceptable range, useful capacity, low DC power, low hardware & deployment costs issues: l2/R2 (beam diffraction) and atmospheric losses, beam blockage
Low communications density (Gb/s/km2) ? → widely spaced hubs Lower deployment costs Long distances, high propagation losses Lower frequencies are much better.
High communications density (Gb/s/km2) ? → densely packed hubs Less Gb/s/hub Short distances, smaller propagation losses Higher frequencies can work well, can provide very high capacity
Research for future high-capacity communications: (1) demonstrate high data rates (2) reduce cost, reduce DC power, increase range and operating margins.

## Slide 10
Systems

## Slide 11: MIMO System Design
More antennas than signal beams: spatial oversampling (averaging).
Given QPSK, 2:1 spatial oversampling:
ADCs/DACs only need 3-4 bits RF/IF/baseband chain needs P1dB only 4 dB above average power
Phase noise requirements similar to single beam system
Efficient digital beamforming using beamspace First compute (low-resolution) spatial FFT. Then cancel crosstalk between closely-spaced users Wideband MIMO arrays: use spatial & temporal FFTs "true time delay"
Beamspace algorithm, Dynamic range: Madhow, UCSB Beamformer ICs: Christoph Studer, ETHZ
M. Abdelghany et al, IEEE Trans. Wireless Comm, Sept. 2021 M. E. Rasekh et al, IEEE Trans. Wireless Comm, Oct. 2021 A. Puglielli et al, 2016 IEEE ICC M. Abdelghany, et. al, , 2019 IEEE SPAWC S. H. Mirfarshbafan et al, IEEE Trans CAS 1, 2020 O Castañeda Fernández et. al, 2021 ESSCIRC M. Abdelghany et al 2019 IEEE GLOBECOM

## Slide 12
Transistors

## Slide 13: Transistors for 100-300 GHz
CMOS: good power & noise up to ~150GHz. Not much beyond. Best published mmwave results at 65-16 nm nodes. InP HBT: record 100-300 GHz PAs, record integrated transceivers SiGe HBT: power better than CMOS, worse than InP HBT GaN HEMT: record power below 100GHz. Bandwidth improving InGaAs HEMT: world's best low-noise amplifiers
Results compiled 8/16/2023

## Slide 14: InP Transistors and ICs
30 nm InP HEMTs: 1.5THz fmax, 1.0THz amplifiers
W. Deal et al., 2016 IEDM (Northrop-Grumman)
130nm InP HBTs: 1.1THz fmax, 3.5V. 670 GHz amplifiers
M. Urteaga, et al., IEEE Device Research Conference, 2011. M. Urteaga, et al., IEEE Proceedings, 2017 (Teledyne, UCSB)
250nm InP HBTs: 650GHz fmax, 4.5V.
Z. Griffith et al., 2007 IPRM conference (UCSB)
M. Urteaga, et al., IEEE Proceedings, 2017 (Teledyne)
THz HBT Scaling Laws
Rodwell, et al., IEEE Proceedings June 2008 (UCSB, Teledyne) Contacts: Baraskar et al., Journal of Applied Physics 2013 (UCSB)

## Slide 15: InP HBT ICs: 60-670 GHz
600 GHz transmitter
670 GHz amplifier
688 GHz fundamental oscillator
570 GHz receiver
208 GHz master-slave latch
529 GHz dynamic divider
M. Urteaga, et al., IEEE Proceedings, 2017 (Teledyne) Z. Griffith et al., IEEE CSICS, 2010 (Teledyne) M. Seo et al., IEICE Electronics Express, 2015 (Teledyne)

## Slide 16: Bipolar Transistor Design
Rodwell, IEEE Proceedings, 2007

## Slide 17: Bipolar Transistor Design: Scaling
Rodwell, IEEE Proceedings, 2007

## Slide 18: Bipolar Transistor Scaling Laws
Narrow junctions. Thin layers High current density Ultra low resistivity contacts
Rodwell, IEEE Proceedings, 2007

## Slide 19: Ultra low resistivity refractory contacts for THz HBTs
32 nm (2.8THz) node requirements
Baraskar et al, Journal of Applied Physics, 2013 (UCSB)
Ohmic contact resistivity: the key challenge for THz HBTs.
Refractory contacts: robust under high-current operation
Low penetration depth: ~ 1 nm
Performance sufficient for 32 nm /2.8 THz node.
Why no ~2 THz HBTs today ? Can't reproduce such base contacts in full HBT process flow.

## Slide 20
InP HBTs: 1.07 THz @ We= 200 nm
?
Rode et al., IEEE TED, Aug. 2015 (UCSB)

## Slide 21: Challenges at the 64nm/2THz & 32nm/3THz Nodes
Baraskar et al, Journal of Applied Physics, 2013
Need high base contact doping >1020/cm3 for good contacts high Auger recombination very low b.
Need moderate contact penetration Pd or Pt contacts react with 3++ nm of base penetrate surface contaminants too deep for thin base
Solution: base regrowth: thin, moderately-doped intrinsic base InGaAs or GaAsSb @ 1019-1020/cm3 thick, heavily-doped extrinsic base P-GaAs, ~1021/cm3
Rode et al., IEEE TED, Aug. 2015

## Slide 22: Regrown-Base InP HBTs: status at end of effort.
Excellent base contacts; but hydrogen base passivation 0.4 W-mm2 resistivity for GaAs/metal contact 290 W sheet resistivity for regrown base  0.60W-mm2 resistivity for InGaAs/GaAs contact✘ 1940W/ sheet resistivity for intrinsic base ✘ (hydrogen anneal needed further adjustment)
Good DC data: even given regrowth refractory Mo/W/TiW emitter contact maintains low rc.
We= 80 nm, Le =5 μm
Y. Fang et al, 2019 IEEE DRC (UCSB)

## Slide 23: Making faster field-effect transistors
III-V FET scaling laws to double bandwidth
Needs: shorter gates thinner channels less resistive contacts thinner (equivalent) gate dielectric greater channel charge
State of art: 32 nm gate length HEMT 1.5 THz fmax (Northrop-Grumman) semiconductor gate dielectric limits further scaling
Further scaling may be feasible target ~2 THz fmax lower Fmin @ 100-300 GHz high-K ZrO2 gate dielectric increased charge: InP channel ?
Scaling laws: Rodwell, IEEE DRC 2010 1.5 THz HEMTs: Deal, 2016 IEDM 1 THz MOS-HEMT: Whitaker, IEEE DRC 2023

## Slide 24: THz InGaAs-channel MOS-HEMT
Gate dielectric: 0.83 nm AlxOyNz / 1.7 nm ZrO2 improved electrostatics vs. ~6 nm InAlAs. potential for improved (ft, fmax) with scaling
Remaining scaling barrier: Limited (low) state density of InGaAs channel Barrier to necessary gm/Wg increase with scaling Theory (right/wrong ?) suggests using InP channel
L. Whitaker et al, 2023 IEEE DRC (UCSB)

## Slide 25: Transistor layouts: I, V, Z, and P.

## Slide 26
IC Design Basics

## Slide 27: 100-300 GHz: transistor requirements, IC design
Transmitters need: high power-added efficiency high added power density (Pout-Pin)/(gate width, emitter length) Receivers need: low cascaded noise
Need reasonable gain/stage. die area, power, accumulated gain compression
At 100-300 GHz, transistor performance is marginal… …how do we design PAs, LNAs, for performance close to transistor limits ?

## Slide 28: Where the IC designer can't help
*If lossless, and given the correct source and load impedances.
mm-wave transistor gain is low: gain-boosting is common Common-source vs. common-gate. Capacitive neutralization. Unconditionally stable positive feedback (Singhakowinta, Int. J. Electronics, 1966)
Such circuits don't improve the parameters that matter the most.
The circuit* doesn't change the transistor minimum cascaded noise figure. (Haus, Adler, Proc. IRE, 1958) The circuit* doesn't change the transistor maximum efficiency vs. added power curve.

## Slide 29: Noise Measure Invariance
H. A. Haus and R. B. Adler, "Optimum Noise Performance of Linear Amplifiers," in Proceedings of the IRE, vol. 46, no. 8, pp. 1517-1533, Aug. 1958. N. Baniasadi and A. M. Niknejad, "Noise Measure Revisited for Design of Amplifiers Close to Activity Limits," in IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 69, no. 6, pp. 2276-2283, June 2022.

## Slide 30: Noise Measure Invariance: Implications

## Slide 31: Cascode LNAs and noise measure invariance

## Slide 32: LNA design for noise close to transistor limit
1) Goal: low noise measure, not noise figure
2) Find bias (J,V) for lowest noise measure
@210GHz, Fcascade,min= 6.57 dB given: Je=0.5 mA/um, Vcb=0.3V
3) Minimum M is independent of circuit configuration*; pick for high bandwidth or high gain/stage (= low PDC)
4) Capacitance in common-base; just like inductance in common-emitter, allows simultaneous tuning for zero reflection coefficient and minimum M.
*HA Haus, RB Adler, Proceedings of the IRE, 1958
5) Write ADS Python code to display source impedance for minimum M.
6) Scale transistor size to eliminate series tuning element. Less input tuning→ less noise from passive element loss.
7) Result: FC,LNA= 7.4 dB (F=7.2 dB, G=13 dB) given FC,transistor= 6.6 dB
<-- all give the same minimum M…
…but common-base gives highest gain (InP HBT @210GHz).
U. Solyu et. al, 2021 EuMIC

## Slide 33: 100-300 GHz Power combining: what is best ?
Direct series-connected M. Shifrin: 1992 IEEE mWave/mmWave Monolithic Circuits Symp. (Raytheon)
Cascaded combining A. Ahmed 2018 EuMIC, 2021 RFIC (UCSB)
Distributed Active Transformer I. Aoki, IEEE Trans MTT, Jan. 2002 (CalTech)
Balun series-connected l/4 baluns: Y. Yoshihara, 2008 IEEE Asian Solid-State Circuits Conference (Toshiba) sub-l/4 baluns: H. Park, et al., IEEE JSSC, Oct. 2014 (UCSB)
Corporate T-line

## Slide 34: On-Wafer Interconnect Losses

## Slide 35: Invariance of PAE vs. added power
Given the correct source and load impedances, all (lossless) power amplifier circuits have the same maximum efficiency vs. added power curve.
Things that don't change PAE: Source/emitter inductance in common-source/emitter Base/gate capacitance in common base/gate. Capacitive neutralization Singhakowinta's unconditionally stable positive feedback.
Design for highest PAE: Pick topology with smallest tuning loss.
Real PAE design: PAE, accumulated gain compression, bandwidth, IM3, …
…which is that of the transistor itself.

## Slide 36: Transistor stacking. Why ? Why not ?
 | Lower frequencies | Higher frequencies
Corporate combining | length → large die area ✘ dB loss → high loss ✘ | length → small die area  dB loss → low loss 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘
 | Lower frequencies | Higher frequencies
Corporate combining |  | 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘

## Slide 37: Cascade Combining: Why ? Why not ?
 | Lower frequencies | Higher frequencies
Corporate combining | length → large die area ✘ dB loss → high loss ✘ | length → small die area  dB loss → low loss 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘
Cascade combining | large interstage matching networks✘ | small interstage matching networks  small # transistor fingers per cell → ok  cascade cell pass-though losses ✘
 | Lower frequencies | Higher frequencies
Corporate combining |  | 
Series-connected | more transistor fingers per cell → ok  | more transistor fingers per cell→ parasitics ✘
Cascade combining | large interstage matching networks✘ | small interstage matching networks  small # transistor fingers per cell → ok  cascade cell pass-though losses ✘

## Slide 38
100-300 GHz ICs

## Slide 39: InP HBT Amplifier: 500 mW, 14.9% PAE, 150 GHz
Alizadeh 2023 IEEE BCICTS
Teledyne 250 nm InP HBT; 2 mm x 1.5 mm
adaptive class-AB bias
combination of corporate and cascade power-combining

## Slide 40: InP HBT Amplifier: 78 mW, 18.4% PAE, 220 GHz
Alizadeh 2024 IEEE MTT Trans. ; to be published
Teledyne 250 nm InP HBT (reduced base post)
Thermally ballasted 4-finger common-base cell: increases maximum Vce.
0.78 mm x 0.75 mm
combination of corporate and cascade power-combining

## Slide 41: Record PAE @ 220 GHz
Key finding: RF breakdown > DC breakdown (thermal effects)

## Slide 42: InP HBT Amplifier: 16.8 dBm, 4.0% PAE, 266 GHz
Ahmed et al, 2021 RFIC
Teledyne 250 nm InP HBT
4-stage capacitively degenerated common-base
Cascade combining: ~40% of Pout from output stage ~40% from driver ~20% from pre-driver.
Improved PAE feasible with re-design, or using 130 nm node

## Slide 43: 200 GHz Low-Noise Amplifier: 130 nm InP HBT
Unpublished data: do not distribute outside this workshop.
5-stage common-emitter design.
F = 6.3-5.5 dB over 180-217 GHz; record for bipolar transistor
-22 dBm IP1dB at 210 GHz.
12-16 dB gain over 170-220 GHz
7 mW DC power dissipation.
Alizadeh, Park, Urteaga, Rowell, Rodwell, to be submitted
Fcascade,LNA = 6.4-5.6 dB

## Slide 44: 210 GHz Transmitter and Receiver ICs
Seo, 2021 IEEE IMS
Size: 2.3 x 0.85 mm2
Size: 2.9 x 0.75 mm2
Teledyne 250nm InP HBT
~ 8.5 dB noise figure
~ 16 dBm Psat
~ 20 GHz bandwidth
~ 20 GHz bandwidth

## Slide 45: 280 GHz Transmitter and Receiver ICs
Soylu; 2023 RFIC, 2023 EuMIC
Teledyne 250nm InP HBT
~ 10-12 dB noise figure
~ 13-14 dBm Psat

## Slide 46
1D and 2D Array Design

## Slide 47: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 48: Do we need 2D arrays ? 1D steering might be fine.
1/sin2f sidelobes provide strong signals to tall buildings.
Providing sidelobes reduces broadside gain by less than 3dB.
→ Don't need 2D arrays to serve tall buildings

## Slide 49: 2D vs. 1D: Don't aim beams in useless directions
With most users on the ground, 2D array wastes spatial degrees of freedom on unoccupied directions. Need some 2D beamsteering to avoid ground reflections.

## Slide 50: 100-300 GHz IC-package connections
type | Frequency | technology | cost | heatsinking
micromachined waveguide interface | 1000 GHz | Research. Cheap one day ? | high ✘ | good
ribbon, mesh bond | 200 GHz | Handcrafted. | high ✘ | good
wafer-scale fan-out package | >200 GHz | Industry standard | low | good
Cu stud flip-chip | >200 GHz | Industry standard | low | ok, marginal for PA ✘
hot vias | 200 GHz | Development | low ? | good
(ball) wirebonds | 100 GHz ✘ | Industry standard | low | good
Deal, IEEE Trans THz, Sept 2011

## Slide 51
140 GHz

## Slide 52: 140 GHz Hub Demonstration
*Modules: Farid et al, IEEE BCICTS 2021, IEEE Trans MTT 2022, Demo: Abu-Surra et. al. (Samsung) 2022 IEEE International Conference on Communications, 16 -20 May 2022, Seoul, Korea
Globalfoundries: 22FDX CMOS Teledyne: 250 nm InP HBT Kyocera: LTCC, assembly
Demonstration (Samsung + UCSB) 8-element receiver*: 22 nm SOI CMOS 8-element transmitter*: 22 nm SOI CMOS + 100 mW InP HBT PAs 2.3 Gb/s @ 120 meters* PTFE lens used to extend link range
Concept: 128 elements, 64 x 10 Gb/s/user, 70 meters.

## Slide 53
210 GHz and 280 GHz ICs, Modules, Links

## Slide 54: Concept: 640 Gb/s, 210 GHz MIMO backhaul
Concept 8 x 80 Gb/s MIMO with 2.1 m baseline 16-element subarrays (7l x 7l antennas) 500 meters range in 50 mm/hr. rain 14 dB margins: (obstruction, operating, aging, packaging) LNAs: 8 dB noise figure
PAs: 50 mW =P1dB
Demonstrated to date: no subarrays, 1 channel
Ongoing demonstration efforts: no subarrays, 4 x 4 MIMO

## Slide 55: 200 GHz link demonstration
8 Gbaud
32 Gb/s
13.4% error vector magnitude → BER < 10-3
attenuator
Soylu, 2023 IEEE BCICTS (UCSB) Teledyne 250 nm InP HBT Kyocera module assembly
Now working towards 4 x 4 MIMO demo.

## Slide 56
What's next: 100-300 GHz

## Slide 57: What's Next ? Large Arrays, Dense Arrays
l/2-pitch 2D arrays at 200-300 GHz Not all systems need 2D arrays, but many do. very small spacing: hard to fit in the circuits Highest-frequency ~ l/2-pitch 2D arrays: 140 GHz CMOS (Rebeiz group, UCSD) Target: large-scale l/2-pitch 220 GHz 2D arrays in InP HBT
Massive inexpensive arrays at 70-140 GHz Motivation: difficulties even with 5G @ 39 GHz Goal: greatly increase Preceived/Ptransmit. longer range, greater margins against blocking and fading.
Approach: greatly increase # transmit, receive elements. low cost: need very low die area per element low DC power: need very low DC power per element

## Slide 58
ICs and Transceivers for 100–300 GHz Wireless

## Slide 59: 100-300 GHz Wireless
Massive (near Tb/s) aggregate capacities: large spectral bandwidths, massive spatial multiplexing .
Limited range: ~100-500 m; atmospheric loss, l2/R2 loss.
Easily-blocked beams: need redundant paths.
IC technologies: CMOS, InP, SiGe (GaN)
Near-term commercial impact: range is too short, cost is too high capacity (Gb/s/km2) is much more than needed
Research (long-term): demonstrate 100+ Gb/s capacity, reduce cost, reduce power, increase range and operating margins. (l/2) pitch arrays at 200+ GHz massive low-cost arrays