## Slide 1: UCSB-E-Phi-dev-1
SOI only: test litho and bonding uniformity

## Slide 2
EPHI – SOI Mask Details – WG Layer

## Slide 3
2X2 and 1X2 MMI

## Slide 4
Directional Couplers and 1X4 MMI
2 sets: DC- 700nm gap, different length
Constant length, gap: 900,800,700,600,500nm

## Slide 5
20GHz Ring resonators
Symmetric design- 500nm spacing.
Resolution markers for loading effect.
Trench and WG widths – 0.7,1,1.5,2 um

## Slide 6
Waveguide Loss cutback structures
3 sets: 1,2,3,4,5 cm?
WG width 0.8,1,2 um

## Slide 7
Bonding Test structures

## Slide 8
90° Bend Loss test structures
Bend radii – 25um 500um – 20 splits

## Slide 9
Mode filters

## Slide 10
Waveguide crossings
No. of crossing – 1,2,4,8,16,32
90°, 75°, 60°, 45°, 30°

## Slide 11
Transitions to Nano-strip waveguide
Si etch – 400nm tip, 800nm strip width

## Slide 12
Taper tips resolution markers
Tip width – 5, 4, 3, 2, 1, 0.5, 0 um

## Slide 13
Straight to bend transition