dept. of electrical and computer engineering

university of california – santa barbara

santa barbara, ca 93106-9560

Phone: (805) 893 3812 x211

fax: (805) 893 8714

facsimile transmittal sheet

to:		from:
Laurie Sullivan		Ilan Ben-Yaacov

company:	phone number:
Photronics Inc.		(805) 893 3812 x211

fax number:	date:
(818) 841-9747		September 17, 2002

Phone number:	re:
(818) 562-8132		Mask Plate Order

address:	total no. of pages including cover:
		5

notes/Comments:

Dear Ms Sullivan,

Please accept this order for one mask plate.

Mask Name: 	CAVET3h

GDSII File Name:	CAVET3h.gds

I can be contacted at the above phone number if there are any problems, or by email at ilan@engineering.ucsb.edu

Regards,

Ilan Ben-Yaacov

CAVET3h – Ilan Ben-Yaacov

Mask Type: 	E-beam	Date:	09/17/02

Material: 	Chrome on Quartz	P.O. number:	006420-6537

Size: 	5”x5”x0.09”	Media type:	FTP folder ftp://ucsbsd@199.36.4.16@207.77.140.1/ilan

Data scale:	1

Mask scale:	1

| TopCell Name | MAIN_D | MAIN_D | MAIN_D | man_1 | dfaswin2 |
| --- | --- | --- | --- | --- | --- |
| GDSII File Name | CAVET3h.gds | CAVET3h.gds | CAVET3h.gds | CAVET3h.gds | CAVET3h.gds |
| Mask Level I.D. | ISO3 | S/D4 | PADISO | Final | Final |
| GDSII Level | 6 | 9 | 12 | 4 | 4 |
| Address Unit | 0.25m | 0.25m | 0.25m | 0.25m | 0.25m |
| Chrome Side Down Reading | R | R | R | R | R |
| Polarity | Pos | Neg | Neg | Neg | Neg |
| Mask C.D. | 6.0 m | - | - | - | - |
| C.D. Tolerance | 0.5 m | 0.5 m | 0.5 m | 0.5 m | 0.5 m |
| Overlay Registration to Grid | 0.25m | 0.25m | 0.25m | 0.25m | 0.25m |
| No. of Defects/Max Defect | 0>5 m | 0>5 m | 0>5 m | 0>5 m | 0>5 m |